## Slide 1
Hard Shoulder Running – Lessons Learned During Design, Construction, and Implementation
Brian Toombs, PE

## Slide 2: Agenda
What is HSR?
Where is HSR Implemented?
Analysis Considerations
  Traffic
  Safety
Cost Considerations
Design Considerations
Implementation
Operations
Screening Process

## Slide 3: What is HSR?

## Slide 4: What is HSR?
The use of the left or right safety shoulder of an existing roadway for travel during certain hours of the day
Preserves shoulder as shoulder during most hours of the day; not a permanent conversion of the shoulder
A TSM&O strategy for addressing congestion and reliability issues; adds capacity only when needed
Various Names
  Hard Shoulder Running
  Shoulder Running
  Temporary Shoulder Use
  Part-Time Shoulder Use

## Slide 5: Origin of HSR
Performance-Based Practical Design
Transportation Systems Management and Operations (TSM&O) Strategies
  Work Zone Management
  Traffic Incident Management
  Service Patrols
  Special Event Management
  Road Weather Management
  Transit Management
  Freight Management
  Traffic Signal Coordination
  Traveler Information
  Ramp Management
  Managed Lanes
  Part-Time Shoulder Use

## Slide 6: Origin of HSR
Active Traffic Management
  Dynamic Speed Limits
  Adaptive Ramp Metering
  Dynamic Lane Assignments
  Queue Warning
  Dynamic Rerouting
  Adaptive Traffic Signal Control
  Dynamic Lane Use/Shoulder Control

## Slide 7: Different HSR Concepts
Left vs. Right
Dynamic vs. Static
Vehicle-Use Options
  All vehicles
  Transit only
  Prohibit trucks
  HOV/HOT
Speed Control Options
  Same speed (as posted)
  Reduced speed

## Slide 8: Where is HSR Implemented?

## Slide 9: Where is HSR Implemented?
States employing Part-Time Shoulder Use in 2016
Source: FHWA

## Slide 10: Where is HSR Implemented?
I-66 in Northern Virginia – Dynamic; Right Side
NJ Turnpike – Static; Right Side

## Slide 11: Where is HSR Implemented?
US 2 in Everett, Washington – Static; Right Side
US 23 in Ann Arbor, Michigan – Dynamic; Left Side

## Slide 12: Analysis Considerations

## Slide 13: Traffic Analysis
Increased Capacity
  Shoulder capacity ranges between 1,000 and 1,650 vehicles per hour
  Dependent on geometric conditions and level of communication to the driver
  Left shoulder capacity is slightly higher than the right shoulder

## Slide 14: Traffic Analysis
HSR Lane Capacity Lower than Freeway Lanes
Highway Capacity Manual (HCM) Analysis
  Cannot adjust capacity on per-lane basis
  Determine new capacity value for the freeway segment
Microsimulation (VISSIM, TransModeler) Analysis
  Can assign capacity and speed on a per-lane basis
  Can prohibit different vehicle classes in HSR lane
  Great tool for public meeting
Recommendation: Use HCM for preliminary analysis and microsimulation for final alternative

## Slide 15: Traffic Analysis
Increased Reliability
  Travel times are more consistent on a daily basis
  Less buffer time required to ensure on-time arrival
  More predictable for users

## Slide 16: Appropriate Length of HSR
Typically Used on Long Segments That Include Multiple Interchanges
  Commuter corridors with recurring congestion
  Used to avoid expensive widening over long corridors
Can Be Used on Acute Bottlenecks
  Georgia and Hawaii use as auxiliary lanes between interchanges
  Termination method is critical to avoid queues

## Slide 17: HSR Lane Termination
End on Basic Freeway Segment as a Lane Drop
  HSR lane merges into adjacent travel lane; ideally at a location where number of mainline lanes are adequate for traffic volume
  Potential to cause queues at merge point
End by Dropping HSR Lane to Interchange Ramp
  HSR lane terminates into an exit-only lane at the interchange
  Ideally a high-volume exit ramp
  Creates a smooth transition of the HSR

## Slide 18: Safety Analysis
How do you predict how HSR will affect safety?

## Slide 19: Safety Analysis – Case Study in Ohio
Ohio’s HSR Project
  Left Side
  Static Operation (4-6pm)
  Variable Speed Limit (45mph)
  Existing Left Shoulder (14-16 ft)
  HSR Lane Width (11.5 ft)

## Slide 20: Safety Analysis – Case Study in Ohio
Initial HSM Analysis Results
 | KA | B | C | O | Total
No Build | 6.5 | 22.0 | 23.2 | 137.1 | 188.9
Build | 7.1 | 23.1 | 24.3 | 142.0 | 196.5
Difference | +0.6 (8%) | +1.1 (5%) | +1.1 (5%) | +4.9 (4%) | +7.6 (4%)
K – Fatal; A – Incapacitating Injury; B – Nonincapacitating Injury; C – Possible Injury; O – Property Damage Only
DON’T PHOTOGRAPH THIS!

## Slide 21: Safety Analysis – Case Study in Ohio
Holes in HSM Analysis
  HSM assumes 24-hour analysis
    HSR is only operational for a few hours per day
  HSM does not account for speed
    HSR is only operational when speeds are lower than free-flow speeds (congestion)
Notes: Analyzing a shoulder in use for part of the day would require knowledge of the hours of operation and the percent of AADT during those hours. Models would be run twice, and a weighted average could be computed

## Slide 22: Safety Analysis – Case Study in Ohio
Countermeasures to prevent fixed object crashes
  Rumble Strips
  Wider Edge Lines
  Median Barrier Reflectors
RUMBLE STRIPS
WIDER EDGE LINE

## Slide 23: Safety Analysis – Case Study in Ohio
Final HSM Analysis Results (with countermeasures)
K – Fatal; A – Incapacitating Injury; B – Nonincapacitating Injury; C – Possible Injury; O – Property Damage Only
 | KA | B | C | O | Total
No Build | 6.5 | 22.0 | 23.2 | 137.1 | 188.9
Build | 5.7 | 18.5 | 19.5 | 142.0 | 185.7
Difference | -0.8 (13%) | -3.5 (16%) | -3.7 (16%) | +4.9 (4%) | -3.2 (2%)

## Slide 24: Safety Analysis – Case Study in Ohio
What do other studies say?
  HSR Would Likely Reduce Congestion-Related Crashes
    Rear-End
  HSR May Increase Crashes Related to Erratic Driver Behavior or Sub-Optimal Geometry
    Fixed Object
    Run-Off-Road
    Sideswipes
Corridors with High Percentage of these Crash Types May Not be Good Candidates for HSR

## Slide 25: Safety Analysis
Summary of Safety Analysis
  HSM Analysis is good, but not perfect
  Additional countermeasures may be necessary
  Review corridor crash patterns before implementation
  Audits have shown safety performance of facilities with HSR is comparable or better

## Slide 26: Cost Considerations

## Slide 27: Cost Considerations of HSR
Compare to Traditional Improvements
  Often less upfront capital cost by often as much as 50%!
  Re-use existing infrastructure saves $$
    Full-Depth Existing Shoulders
    Existing Fiber Backbone
    Existing Freeway Management System

## Slide 28: However………
HSR typically incur a greater proportion of costs as continuing operations and maintenance
ITS infrastructure often has a much shorter anticipated useful life than traditional improvements
Could result in future funding gaps or the inability to properly operate and maintain system

## Slide 29: Benefit/Cost Analysis of HSR
Include the following for Costs:
  Capital Cost – upfront cost of project improvement
  Operations & Maintenance Cost – continuing cost necessary to operate and maintain, including labor costs for activities such as emergency patrols & TMC staff
  Replacement Cost – periodic cost of replacing or redeploying equipment as it becomes obsolete and reaches an end of its expected useful life

## Slide 30: Benefit/Cost Analysis of HSR
Typical Benefits:
  Reduced Travel Times
  Reduced Delay
  Reduced Fuel Consumption
  Reduced Number of Crashes
To Monetize Benefits, FHWA TOPS-BC tool is a good source
  Spreadsheet-based tool
  HSR is one of the strategies – identified as ATDM Hard Shoulder Running

## Slide 31: Design Considerations

## Slide 32: ITS Design – CCTV Cameras
No Blindspots
  Number of cameras depends on horizontal geometry (curves), vertical geometry, bridge overpasses, overhead signs

## Slide 33: ITS Design - Gantries
Spacing Varies Between ½ and 1 Mile
  Function of existing overhead guide sign locations and overhead bridge crossings
  Number of ramps
Spacing Depends on their Function
  Speed Harmonization
  Incident Management
  Dynamic Operation
Recommendation: Walk the corridor early in the project and identify preliminary locations of gantries

## Slide 34: ITS Design – Dynamic Message Signs
Several Options
  Individual Bricks
  Full-Width Signs
Mounting Options
  Truss
  Cantilever
Notes: Often this comes down to a choice of maintenance options – catwalk vs accessing from a bucket truck from the highway. Comes down to whether to close a lane on the highway or not.

## Slide 35: ITS Design – Put It All Together
Notes: Often this comes down to a choice of maintenance options – catwalk vs accessing from a bucket truck from the highway. Comes down to whether to close a lane on the highway or not.

## Slide 36: Geometric Design
Key Criteria for HSR:
Lane Width
Shoulder Width/Lateral Offset to Obstruction
Cross Slope/Crown Line Location
Vertical Clearance
Posted Speed

## Slide 37: Geometric Design – Cross Slope
Notes: What do you do on the high-side of superelevation, especially when it crosses over a bridge? Do you rebuild the existing shoulder to introduce some cross slope in the proper direction for the horizontal curve, which would require partial redecking of the existing bridge, or do you allow a variance for cross slope and potentially introduce a safety issue?

## Slide 38: Geometric Design – Cross Slope
Notes: What do you do on the high-side of superelevation, especially when it crosses over a bridge? Do you rebuild the existing shoulder to introduce some cross slope in the proper direction for the horizontal curve, which would require partial redecking of the existing bridge, or do you allow a variance for cross slope and potentially introduce a safety issue? What about the existing median barrier? Does that need to be replaced as well? And we have now pinched the vertical clearance by 10” in the shoulder lane in the superelevation section. Is that a problem?

## Slide 39: Pavement Design
Existing Shoulder Pavement Depth
Concrete vs. Asphalt
  Construction Methods
  Joints
Vehicle Usage in HSR
  Limit Trucks

## Slide 40: Implementation

## Slide 41: ConOps & Systems Engineering Analysis

## Slide 42: Design Exceptions
Needed if Minimum Controlling Criteria is not met
Explain why it is infeasible to meet Controlling Criteria
Identify Mitigation Strategies
  Reduced Speeds
  Increased Patrol
  Prohibit Trucks
  Emergency Pull-Offs
  Rumble Strips
  Wider Pavement Markings
  Barrier Reflectors
Engage FHWA Early and Often!

## Slide 43: Stakeholder Engagement
Wide Range of Stakeholders
  Planning, Operations, Design, Maintenance staff with DOT
  Law Enforcement
  Emergency Responders
  Transit Agency
  MPO Staff
  Local Agency
  FHWA Division Office
Education and Outreach
  Workshops
  Peer Exchanges
Notes: Get the right players at the table; discuss emergency response and incident management concerns; discuss maintenance concerns; discuss transit operation concerns (if applicable)

## Slide 44: Public Involvement
General Reaction
  Unfamiliarity with the concept
  What are the Details (is the shoulder open/closed, how do I know when to get in, is speed limit changing, what if I break down?, etc.)
Workshops, Forums, Local Council Meetings
  Commuter traffic
Various Media Campaigns
Notes: Depending on the site however, may be a lot of commuter traffic – getting them to public meetings may be difficult

## Slide 45: Public Outreach
Michigan DOT

## Slide 46: Operations

## Slide 47: Law Enforcement
Enforcement of improper lane usage and speed violators challenging
  Congestion
  Where to pull over violators
Maintaining a shoulder to pull off is critical
During plan development, have Law Enforcement tour the TMC
Engage Early!

## Slide 48: Emergency Pull-Offs - Virginia

## Slide 49: Emergency Pull-Offs - Michigan
Notes: Michigan identifies all of their shoulder pull-off areas (this one identified as 47N) for quicker response time. Notice that Michigan has a left-shoulder HSR lane but uses their pull-offs on the right side where there is already a “wide” shoulder. This was done as mitigation for their Design Exception. Not always practical………

## Slide 50: System Start-Up – Daily Sweep

## Slide 51: Incident Management
Notes: If the incident occurs at the end of the SmartLANE corridor, advanced signing warning drivers of an incident and indicating that the lane will be closing can be given using the 9 overhead gantry signs and 1 cantilever sign at the beginning of the project.

## Slide 52: Screening Process

## Slide 53: Screening Process - Planning
Is HSR consistent with region’s long-range plan?
What is the transportation need in the corridor?
Does the region have experience with TSM&O strategies?
Is HSR feasible from a constructability standpoint?
Is real-time monitoring and incident response in place?
What are the impacts?
Does HSR implementation reduce cost compared to traditional projects?
How can HSR be designed and operated to optimize benefits and mitigate impacts?

## Slide 54: Screening Process – Pre-Engineering
Does the paved shoulder width meet minimum widths for carrying traffic?
  If not, lower speeds or prohibit trucks?
Do bridges over the shoulder meet minimum clearance height requirements?
  If not, special vehicle-height restrictions necessary?
Is the shoulder pavement depth sufficient for carrying traffic?
  If not, prohibit trucks/heavy vehicles?
Is the drainage system compatible with shoulder use?
  If not, modify drainage or lower speeds?

## Slide 55: Screening Process – Pre-Engineering
Do the bridges along the corridor provide enough lateral width for shoulder use?
  If not, is widening an option?
Is the length of the HSR segment long enough to provide meaningful congestion relief?
  If not, is the segment addressing an acute bottleneck?
Can safety concerns be resolved?
  Can ramp merge visibility and merging distance issues be resolved?
  Can substandard geometry be mitigated through lower speeds, vehicle restrictions, or ATM?
  Can the concerns of emergency first-responders and maintenance personnel be resolved?

## Slide 56: Potentially Good HSR Candidates
Reliable and repeatable periods of congestion
Lateral width to accommodate HSR implementation
Minimal widening of bridges along the corridor
Minimal corrections to overhead bridges in order to fit the HSR cross section under
Prefer a long corridor for HSR implementation
Prefer full-depth existing shoulders
Prefer ITS-compatible corridor
Prefer tangential alignments or horizontal curves where HSR is on the outside
Prefer to minimize R/W impacts

## Slide 57: Questions?
Contact:
Brian Toombs, PE
Burgess & Niple, Inc.
614.459.2050 (o)
614.946.9343 (c)
Brian.toombs@burgessniple.com

## Slide 58: Extra Slides

## Slide 59: Where is HSR Implemented?
Source: FHWA (Use of Freeway Shoulders for Travel)

## Slide 60: Where is HSR Implemented?
I-95 in Boston, Massachusetts – Static; Right Side
Notes: Site in Boston limits the shoulder use to just cars. They are also in the process of widening I-95 to accommodate a permanent lane so they are slowly phasing out the HSR implementation here

## Slide 61: HSR Lane Termination
Existing Lane
New Perm. Lane
HSR/Ex. Shoulder

## Slide 62: Safety Analysis – Case Study in Ohio
Chart: 
| Fixed Object | Sideswipe - Passing | Rear End | Injury Crashes
Below Statewide Average | 0.142 | 0 | 0 | 0.238
Statewide Average | 0.119 | 0.186 | 0.299 | 0.003
Above Statewide Average | 0 | 0.087 | 0.19 | 0
67 Crashes
138 Crashes
77 Crashes
40 Crashes
Crashes along EB I-670 between 2014 and 2016 (282 Total Crashes)

## Slide 63: Public Outreach
Washington DOT
Virginia DOT

## Slide 64: Incident Management
Notes: Incident Management

## Slide 65: Incident Management
Notes: Multi-Purpose DMS to improve communication to drivers

## Slide 66: Incident Management - Ohio
Notes: If the incident occurs near the beginning of the SmartLANE corridor, advanced signing warning drivers of an incident and indicating that the lane will be closing can be given; once the driver is past the incident, notice that the lane is back open to drivers.

## Slide 67: Incident Management - Ohio
Notes: These overhead gantries are also beneficial during off-peak (when the SmartLANE isn’t open). They can be used to warn drivers of temporary lane closures along the corridor; again notice that once past the incident, the lane(s) are open to traffic again. NOTE: the yellow merge arrows are not yet approved for use by FHWA (not in the MUTCD) but the team is working on that. If they aren’t approved for this project, a yellow “X” would be used instead.
All of this requires extensive system programming and training for the personnel

## Slide 68: Other State’s Lessons Learned

## Slide 69: Lessons Learned - Michigan
Keep It Simple
  Software can be complicated; simplify the number of strategies
  External controller for the DMS allows easier maintenance and smaller/cheaper signs
Budget Actual Costs of Project
  Include maintenance costs when determining budget
  Include training budget for TMC personnel
Engage FHWA
  Coordinate with FHWA early in the project

## Slide 70: Lessons Learned - Virginia
Work Closely with FHWA
  Design Exception Process
  Systems Engineering Analysis (SEA)
  Conceptual Operations (ConOps)
Better Public Engagement
  VDOT completed Public Involvement in-house
  Utilize staff that communicate well to ALL users, not just engineers; reach all users through technology
Emergency Responders
  Engage during design to ensure they are accommodated

## Slide 71: Lessons Learned - Minnesota
Engaged FHWA early
  Design Exception process went smoothly
Multiple Strategies for Operations
  Several for inclement weather
  Several for various incidents
  Several for various levels of congestion
  Became challenging getting operators trained
Public Involvement
  Completed this in-house
  Struggled to get education out to all users prior to opening

## Slide 72: Lessons Learned - Washington
FHWA Engagement
  Didn’t engage them early enough in the project process
Documentation
  Filed several design variances
  Needed good documentation of the variances
  Needed good justifications for the variances
Public Involvement
  Completed this in-house
  Struggled to get education out to all users prior to opening