## Slide 1: The 2016 William S. Gulick Project Excellence Award

## Slide 2: KY 30 TRAVELLERS REST RECONSTRUCTION PROJECT
district 10
design section

## Slide 3: PROJECT TYPICAL SECTION
DESIGN CRITERIA | EXISTING | FINAL
# OF LANE | 2 | 2
PAVE WIDTH | 20’ | 22’
SHLD WIDTH | 1’ | 10’
BRIDGE WIDTH | 20’ | 42’
MIN. RADIUS | 159.2’ | 965’
MAX. GRADE | 5.2% | 5%
MIN. SIGHT D. | 200’ | 495’

## Slide 4
Interstate 75- Mountain Parkway Corridor
KY 30 Sections, 10-279.60, 10-1084, and 10-279.51
10-279.60
10-279.51
10-1084.00
LEVI
TYLER
JACKSON COUNTY
OWSLEY COUNTY
BOONEVILLE
10-1084
Selected
ALTERNATE 1
ALTERNATE 2
10-279.60
10-279.51
PROPOSED
ALIGNMENT
EXISTING
ALIGNMENT
TRAVELLERS
REST
10-1084.00

## Slide 5: EXISTING CONDITIONS
Existing bridge with structural rating of 8.3
Poor horizontal and vertical alignments at bridge approaches.
Debris pile up at the center pier.
If replaced at current location, would not be used with new KY 30 corridor
10-1084.00

## Slide 6: PROJECT Considerations
10-1084: Originally a bridge replacement project
During Preliminary Line and Grade Project team evaluated and discussed the London (Interstate 75)- Mountain Parkway Corridor reconstruction and this project lays within the proposed corridor.
10-1084 falls between two KY 30 reconstruction projects that’s part of the London – Mountain Parkway Corridor, 10-279.51 and 10-279.60.
Project team decided to go with the alternate that can be tied into the proposed London-Mountain Parkway corridor.
10-279.51: Reconstruction of KY 30 from Travellers Rest to Levi. Currently under construction
10-279.60: Reconstruction of KY 30 from Tyler to Travellers Rest. The Owsley County section (10-279.61) moving to phase 2.
10-1084.00

## Slide 7: CONSTRUCTION
10-1084.00

## Slide 8: Thank you
10-1084.00

## Slide 9: US 231, BUTLER COUNTY

## Slide 10: EXISTING 8’ X 6’ BOX CULVERT
EXISTING OUTLET

## Slide 11: PROPOSED 8’ X 6’ BROKEN BACK BOX CULVERT
2:1 broken back box culvert
Outlet (looking up stream)

## Slide 12: 8’ X 6’ BOX CULVERT
CONTRA COSTA ENERGY DISSIPATER

## Slide 13: UTILITY COORDINATION
FIBER OPTIC LINE SUPPORTED DURING CONSTRUCTION
FIBER OPTIC LINE CONCRETE DUCT RE-CONSTRUCTED

## Slide 14: RETAINING WALL
BEFORE
AFTER

## Slide 15: US 231 LOOKING NORTH
BEFORE
AFTER

## Slide 16: 12-1085 KY 777 Bridge Replacement at Garrett Floyd County
Notes: Lastly is a District 12 project submitted by Chris James.

## Slide 17: Project Location
KY 80
Project Location
To Prestonsburg
Notes: One of the most interested aspects of this submittal is the narrative from a Bridge’s point of view.
The bridge gave it’s autobiography, mentioning that it was bypassed so to speak when KY -80 was reconstructed in the late 1970’s.

## Slide 18: Existing Conditions
One-Lane Steel Truss Bridge
  Approx. 11.5’ wide with 3.5’ sidewalk
  Single Span (approx. 100’)
  Opening Area = 1,471 sq. ft.
  Sufficiency Rating = 3
  Built in 1944
    Eligible for National Register of Historic Places
Approx. 16’-18’ wide approaches
ADT
  2008: 640
  2028: 800
Notes: Bridge was still used to primarily access the old high school which later relocated a few miles away as Allen Central and the old building was demolished. There was consideration of removing the bridge completely. Through public outcry via Facebook and the need to provide alternate access to baseball field, walking track, and picnic shelters it was decided to keep the crossing.

## Slide 19
Notes: Connection from downtown Garrett to park.

## Slide 20: Alternates
 | Right of Way | Utilities | Construction | TOTAL
Alternate 1 – Repair Existing | $48,500 | $35,000 | $730,400 | $813,900
Alternate 2 – Spread Box Beam Bridge | $159,700 | $45,000 | $643,617 | $848,317
Alternate 3 – Thru-Girder Bridge | $152,200 | $40,000 | $898,216 | $1,090,416
Alternate 4 – Truss Bridge | $152,200 | $40,000 | $1,068,301 | $1,260,501
Low traffic volumes utilizing the bridge
Emphasis to preserve truss bridges
Based on structural inspection, relatively good condition of truss
Lowest project cost of all alternates
Alt. 1-Preferred
Notes: Alts considered.

## Slide 21: Deck Removal
Deck Reconstruction
Paint Process
Approach Work
Notes: Bridge received a new deck.

## Slide 22: Approach Work
Nearly Completed
Notes: Interesting is that the bridge was going to be orange to which the bridge responded “What is this, Tennessee?” Orange was the school color of the old Garrett High school.

## Slide 23: Finished Bridge
Notes: Fortunately contract could not obtain this color as specified in the contract so became a brighter blue version of the previous version. A great story and another great project. Now for this years recipient of the 2015 Project Excellence Awards………

## Slide 24
District 5
Item 5-371.12
Jefferson County
Springcrest Drive
Culvert Replacement

## Slide 29: The 2016 William S. Gulick Project Excellence Award goes to …???