## Slide 1: Roadway Intersections Database
09-07-16
Eric Green, PE, GISP
Jason Blackburn, PE
Lindsay Walker, PE, PTOE, AICP
Kentucky
Transportation
Center

## Slide 2: Agenda
Development of the Database
  Background
  Database Description
  Safety Analysis
Reason for Planning Study
Planning Study Process
Wrap-up
  Current Project Status
  Issues and Limitations
  Additional Uses

## Slide 3: Background
Approximately 35 percent of all traffic crashes in Kentucky occur at intersections
There is a need to prioritize intersection crashes
Kentucky’s Highway Safety Improvement Program ranks these intersections
Crashes are not always properly located
  Lat/long or Linear Reference System

## Slide 4: The New Methodology
Create a maintainable spatial intersection database
Use with SafetyAnalyst and Safety Performance Functions
Tied to KYTC’s node usage table (changes are propagated)
Dynamically linked to traffic volumes and road geometry
Other users: planning, maintenance, IT (not just safety)
Includes all roads (state and local)
Includes an area of influence

## Slide 5: HSM Intersections

## Slide 6: Merge or Not

## Slide 7: Approach Counts
Count the number of s/e points for each unique route ID
Odd = 1 approach (route terminates)
Even = 2 approaches (route enters & exits)
Subsidiary Route-Type (NC, Y, Crossovers) = No approaches

## Slide 8
2
1
2
2
2
2
KY 1211 = 5, 1 approach
US 60 = 6, 2 approaches

## Slide 9: Calculating Entering Traffic
If TYPE_OP = 1 and Knu_S_E = ‘S’, entering traffic = LAST_COUNT*1
If TYPE_OP = 1 and Knu_S_E = ‘E’, entering traffic = LAST_COUNT*0
If TYPE_OP = 2 or TYPE_OP = D, entering traffic = LAST_COUNT*0.5

## Slide 10: Mapping the Results

## Slide 11
Type | Code | Description | Count
1 | U3rF | undivided 3-leg rural full stop | 78
2 | U3rP | undivided 3-leg rural (at least) partial stop | 37256
3 | U3rS | undivided 3-leg rural signal | 96
4 | U3uF | undivided 3-leg urban full stop | 68
5 | U3uP | undivided 3-leg urban (at least) partial stop | 10252
6 | U3uS | undivided 3-leg urban signal | 583
7 | U4rF | undivided 4+ leg rural full stop | 77
8 | U4rP | undivided 4+ leg rural (at least) partial stop | 4202
9 | U4rS | undivided 4+ leg rural signal | 166
10 | U4uF | undivided 4+ leg urban full stop | 89
11 | U4uP | undivided 4+ leg urban (at least) partial stop | 2484
12 | U4uS | undivided 4+ leg urban signal | 1492
13 | D3rP | divided 3-leg rural (at least) partial stop | 729
14 | D3rS | divided 3-leg rural signal | 26
15 | D3uP | divided 3-leg urban(at least) partial stop | 1292
16 | D3uS | divided 3-leg urban signal | 335
17 | D4rP | divided 4+ leg rural (at least) partial stop | 459
18 | D4rS | divided 4+ leg rural signal | 66
19 | D4uP | divided 4+ leg urban(at least) partial stop | 560
20 | D4uS | divided 4+ leg urban signal | 832

## Slide 12: Safety Analysis

## Slide 13: Intersection Priority List
Need to rank all intersections by a safety factor
Replace the traditional and inadequate Critical Rate method
  Regression-to-the-mean
  Relationship between AADT and crashes
Employ state-of-the-art methodologies of the Highway Safety Manual

## Slide 14: Regression To The Mean
  Sir Francis Galton, 1887
    Sweet pea seed size in successive generations
Mean
Federal Highway Administration
U.S. Department of Transportation

## Slide 15: Safety Performance Function

## Slide 16: Model Development
20 SPFs developed for each intersection type
Each model included SPFs for all and KAB crashes
SPFs and observed crashes were used to calculate a new measure of safety…

## Slide 17: Potential for Crash Reduction
Observed Crashes
EB Crashes (Corrected)
Predicted Crashes from SPF
PCR
Crashes per year
AADT
Notes: Note that all of for specific site

## Slide 18
Sort by PCR
Filter by county or District
Calculate the PCR for a new intersection using SPF

## Slide 19: Reason For Study
(Jason rambles on for a couple of minutes.)

## Slide 20: District 10 Intersections Study

## Slide 21: Study Components
Existing Conditions
  Intersection Geometry
  Manner of Collision
  Traffic Volumes
Improvement Development
  HSIP Funded Projects (<$500,000)
  PIF Projects
  Short-Term Line Items
Cost Estimation
Documentation
Contract Ready Plans

## Slide 22: Purpose and Need
Purpose
  To identify potential improvements at 50 identified intersections throughout KYTC District 10.
Need
  Sight Distance Issues
  Multiple Access Points
  Signage and Striping
Goals and Objectives
  Improvement options that address identified safety issues
  Construction quantities and cost estimates
  Solutions that are less than $500,000 where possible

## Slide 23: Study Area

## Slide 24: Terms
Critical rate factor (CRF)
  Crash rate for a spot or segment divided by the critical crash rate
KAB
  Injury scale
    K = Fatal
    A = Incapacitating Injury
    B = Non-incapacitating Injury
Potential Crash Reduction (PCR)
  Estimate of crash frequency reduction

## Slide 25: Intersections
Top 5 have highest fatality and injury collision rate (KAB)
Next 41 ranked in order by PCR
Last 4 were identified as locations with safety issues by the District

## Slide 26: Crash Rates
Chart: 
All Crashes | 9 | 30 | 16 | 27 | 4 | 35 | 15 | 13 | 10 | 9 | 9 | 8 | 15 | 7 | 17 | 27 | 8 | 8 | 7 | 6 | 6 | 6 | 18 | 6 | 6 | 6 | 9 | 5 | 5 | 5 | 14 | 5 | 5 | 5 | 6 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 2 | 2 | 1 | 0
PCR | 3.5173 | 7.0597 | 7.0127 | 12.6054 | -0.26846 | 18.7602 | 7.4278 | 6.7837 | 5.2767 | 4.6022 | 4.5084 | 3.9604 | 3.6733 | 3.5212 | 3.4746 | 3.4235 | 3.1924 | 3.1193 | 2.966 | 2.8535 | 2.8384 | 2.7954 | 2.7449 | 2.6871 | 2.6636 | 2.5219 | 2.3653 | 2.2119 | 2.1841 | 2.1473 | 2.1169 | 2.0024 | 1.9969 | 1.9246 | 1.9164 | 1.6325 | 1.6322 | 1.6173 | 1.5952 | 1.5879 | 1.5594 | 1.5508 | 1.5265 | 1.5122 | 1.5098 | 1.5031 | 0.58221 | 0.42959 | 0.19046 | -0.07133
CRF | 2.6292 | 1.4692 | 2.2429 | 26.6193 | 4.0798 | 2.048 | 2.1354 | 1.7148 | 3.1224 | 2.6458 | 2.8101 | 3.9516 | 1.4861 | 3.3556 | 1.0263 | 1.6375 | 1.7341 | 2.4855 | 2.1756 | 4.0464 | 2.6124 | 2.3412 | 0.9077 | 3.8717 | 7.3224 | 12.85 | 1.4225 | 6.5341 | 2.316 | 2.1328 | 1.8103 | 4.4433 | 2.7003 | 2.4295 | 1.172 | 2.8967 | 2.816 | 6.4602 | 3.8183 | 2.1799 | 4.4722 | 4.442 | 0.87914 | 3.1027 | 6.7825 | 3.3935 | 4.0375 | 4.8129 | 2.5237 | 0

## Slide 27: Improvement Categories
Signage & Striping: 30
Sight Distance: 9
Delineation: 14
Traffic Signals: 5
Turn Lanes: 13
Access Management: 25
Realignment: 19

## Slide 28: Improvement Considerations
Adjacent Intersections
  Consistent Typical Section
  Consistent Speed
Access Management Study
Multiple Options
Line Items for Individual Improvements

## Slide 29: Example Projects

## Slide 30: Project Cost Distribution
Projects < $500,000
33
Projects > $500,000
17 May Require PIF
6 Have Options < $500,000

## Slide 31: Additional Study Components
Crash Distribution
Signal Warrant Analysis
Detailed Cost Estimates
Standard Drawings

## Slide 32: Summary Table
County | Intersection # | Cross Streets | Treatments |  |  | Design | Right-of-Way | Utilities | Construction | Total Cost
Magoffin | 36-2 | KY 40 at Coal Branch Road | A | Realignment | Shift intersection away from building to improve sight distance. | $50,000 | $48,000 | $25,000 | $81,600 | $205,000
 |  |  | B | Widening | Widen Coal Branch Road. |  |  |  |  | 
 |  |  | C | Signs | Install "No Parking" signs (R8-3a) in front of the bank on KY 40. | N/A |  |  | $400 | 
Magoffin | 36-3 | KY 40 at Coal Branch Road | A | Signs | Sign Coal Branch Road to be one-way. | $50,000 | $75,000 | $15,000 | $109,600 | $250,000
 |  |  | B | Realignment | Widen and realign Flint Street and Higgin Street to accommodate new traffic pattern. |  |  |  |  | 
 |  |  | C | Signs | Install "No Parking" signs (R8-3a) in front of the bank on KY 40. | N/A |  |  | $400 | 
Breathitt | 37-1 | KY 15 at Thorpe Road | A | Pavement | Add full lane rumble strips to slow vehicles through curve. | $50,000 | $55,000 | $15,000 | $360,000 | $480,000
 |  |  | B | Sight Distance | Improve sight distance with slope removal near corner of Thorpe Road. |  |  |  |  | 
Breathitt | 37-2 | KY 15 at Thorpe Road | A | Pavement | Add new roadway between Thorpe Road and Fish Pond Loop. | $50,000 | $300,000 | $25,000 | $180,000 | $555,000
 |  |  | B | Access Management | Close Thorpe Road and access points between Thorpe Road and Fish Pond Loop. |  |  |  |  | 
Menifee | 38-1 | US 460 at KY 746 | A | Delineation | Add delineators to require utilization of the center turn lane. | $50,000 | $0 | $10,000 | $45,300 | $106,000
 |  |  | B | Pavement | Add left turn receiving pocket on US 460. |  |  |  |  | 
 |  |  | C | Pavement | Paint stop bar on KY 746. | N/A |  |  | $700 | 
Menifee | 38-2 | US 460 at KY 746 | A | Access Management | Close access points on east side of US 460. | $50,000 | $0 | $10,000 | $13,300 | $74,000
 |  |  | B | Pavement | Paint stop bar on KY 746. | N/A |  |  | $700 | 
Wolfe | 39 - 1 | KY 15 at Swift Camp Creek | A | Pavement | Add SB left turn pocket. | $200,000 | $0 | $10,000 | $761,000 | $1,090,000
 |  |  | B | Access Management | Realign Swift Camp Creek Road. | $50,000 |  |  | $69,000 | 
Wolfe | 39 - 2 | KY 15 at Swift Camp Creek | A | Access Management | Close road access and provide driveway for resident only. | $50,000 | $0 | $0 | $35,000 | $85,000
Perry | 40 - 1 | KY 15 at Scuddy Mountain Rd. | A | Pavement | Install Stop signs and stop bar on driveways. | N/A | $0 | $10,000 | $3,100 | $250,000
 |  |  | B | Pavement | Re-stripe dedicated left turn lanes on KY 15. | N/A |  |  | $39,100 | 
 |  |  | C | Pavement | Improve access for Scuddy Branch Road. | $50,000 |  |  | $147,800 | 
Perry | 40 - 2 | KY 15 at Scuddy Mountain Rd. | A | Pavement | Install stop signs and stop bar on driveways. | N/A | $10,000 | $15,000 | $3,100 | $305,000
 |  |  | B | Pavement | Re-stripe dedicated left turn lanes on KY 15. | N/A |  |  | $39,400 | 
 |  |  | C | Pavement | Change access to Scuddy Mountain Road from Scuddy Branch Road. | $50,000 |  |  | $187,500 | 
Wolfe | 41 | KY 191 at KY 746 | A | Sight Distance | Trim trees inside of curve on KY 191. | N/A | $10,000 | $25,000 | $2,700 | $295,000
 |  |  | B | Realignment | Realign for 90 degree intersection. | $50,000 |  |  | $207,300 | 
 |  |  | C | Realignment | Extend driveway to access center of the curve. |  |  |  |  | 
Perry | 42 | KY 476 at KY 1146 | A | Signs | Move stop sign on KY 1146 closer to intersection. | N/A | $0 | $35,000 | $800 | $335,000
 |  |  | B | Pavement | Add stop bar on KY 1146. | N/A |  |  | $700 | 
 |  |  | C | Delineation | Delineate KY 476 from parking area. | $50,000 |  |  | $248,500 | 
Link

## Slide 33: Crash Distribution

## Slide 34: Detailed Cost Estimates
ITEM | BID CODE | UNIT | UNIT PRICE | INT1 |  | INT1 |  | INT1 |  | INT1 | 
 |  |  |  |  |  | OPTION 1-D (ACCESS) |  | OPTION 2 |  | OPTION 2-D (ACCESS) | 
 |  |  |  | QUANTITY | TOTAL | QUANTITY | TOTAL | QUANTITY | TOTAL | QUANTITY | TOTAL
DGA BASE | 00001 | TON | $20.00 | 63 | $1,259.25 | 0 | $0.00 | 226 | $4,520.11 | 76 | $1,527.20
CEMENT STABILIZED ROADBED | 00008 | SQ YD | $3.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00
DRAINAGE BLANKET-TYPE II-ASPH | 00018 | TON | $43.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00
ASPHALT SEAL AGGREGATE | 00100 | TON | $95.00 | 2 | $228.00 | 0 | $0.00 | 5 | $457.27 | 0 | $0.00
REMOVE CONCRETE MEDIAN | 23839EC | SQ YD | $47.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00
RELOCATE LIGHT POLE | 23836EC | EACH | $4,000.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00
SAW CUT | 20430ED | LF | $3.40 | 630 | $2,142.00 | 400 | $1,360.00 | 400 | $1,360.00 | 400 | $1,360.00
THERMO RUMBLE STRIPS TY 2 | 24097EC | LF | $30.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00
DOUBLE 4' X 4' RCBC | N/A | LF | $460.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00
6X5 BOX CULVERT | N/A | LF | $400.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00
EXTEND 10X6 BOX CULVERT | N/A | LF | $1,400.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00
10X6 BOX CULVERT HDWL | N/A | EACH | $7,500.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00
REDI ROCK/STRONG TIE RETAINING WALL | N/A | EACH | $45.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00
NEW LIGHTED INTERSECTION | N/A | EACH | $65,000.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00
PERMANENT DRAINAGE EASEMENT |  | ACRES |  | 0 |  | 0 |  | 0 |  | 0 | 
RIGHT OF WAY |  | ACRES |  | 0.135 |  | 0 |  | 0.233 |  | 0.233 | 
TEMPORARY EASEMENT |  | SQ FT |  |  |  |  |  |  |  |  | 
 |  |  | CONSTRUCTION COSTS SUBTOTAL: |  | $4,000 |  | $2,000 |  | $7,000 |  | $3,000
MOBILIZATION (ROUNDED UP TO $1000) | 02568 | LS | 3% |  | $1,000 |  | $1,000 |  | $1,000 |  | $1,000
DEMOBILIZATION (ROUNDED UP TO $1000) | 02569 | LS | 1.50% |  | $1,000 |  | $1,000 |  | $1,000 |  | $1,000
 |  |  | SUBTOTAL: |  | $6,000 |  | $4,000 |  | $9,000 |  | $5,000
 |  |  | CONTINGENCY (20%): |  | $2,000 |  | $1,000 |  | $2,000 |  | $1,000
 |  |  | TOTAL: |  | $10,000 |  | $5,000 |  | $20,000 |  | $6,000
Link

## Slide 35: Detailed Cost Estimates
ITEM | BID CODE | UNIT | UNIT PRICE | INT1 |  | INT1 |  | INT1 |  | INT1 | 
 |  |  |  |  |  | OPTION 1-D (ACCESS) |  | OPTION 2 |  | OPTION 2-D (ACCESS) | 
 |  |  |  | QUANTITY | TOTAL | QUANTITY | TOTAL | QUANTITY | TOTAL | QUANTITY | TOTAL
DGA BASE | 00001 | TON | $20.00 | 63 | $1,259.25 | 0 | $0.00 | 226 | $4,520.11 | 76 | $1,527.20
CEMENT STABILIZED ROADBED | 00008 | SQ YD | $3.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00
DRAINAGE BLANKET-TYPE II-ASPH | 00018 | TON | $43.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00
ASPHALT SEAL AGGREGATE | 00100 | TON | $95.00 | 2 | $228.00 | 0 | $0.00 | 5 | $457.27 | 0 | $0.00
REMOVE CONCRETE MEDIAN | 23839EC | SQ YD | $47.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00
RELOCATE LIGHT POLE | 23836EC | EACH | $4,000.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00
SAW CUT | 20430ED | LF | $3.40 | 630 | $2,142.00 | 400 | $1,360.00 | 400 | $1,360.00 | 400 | $1,360.00
THERMO RUMBLE STRIPS TY 2 | 24097EC | LF | $30.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00
DOUBLE 4' X 4' RCBC | N/A | LF | $460.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00
6X5 BOX CULVERT | N/A | LF | $400.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00
EXTEND 10X6 BOX CULVERT | N/A | LF | $1,400.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00
10X6 BOX CULVERT HDWL | N/A | EACH | $7,500.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00
REDI ROCK/STRONG TIE RETAINING WALL | N/A | EACH | $45.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00
NEW LIGHTED INTERSECTION | N/A | EACH | $65,000.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00 | 0 | $0.00
PERMANENT DRAINAGE EASEMENT |  | ACRES |  | 0 |  | 0 |  | 0 |  | 0 | 
RIGHT OF WAY |  | ACRES |  | 0.135 |  | 0 |  | 0.233 |  | 0.233 | 
TEMPORARY EASEMENT |  | SQ FT |  |  |  |  |  |  |  |  | 
 |  |  | CONSTRUCTION COSTS SUBTOTAL: |  | $4,000 |  | $2,000 |  | $7,000 |  | $3,000
MOBILIZATION (ROUNDED UP TO $1000) | 02568 | LS | 3% |  | $1,000 |  | $1,000 |  | $1,000 |  | $1,000
DEMOBILIZATION (ROUNDED UP TO $1000) | 02569 | LS | 1.50% |  | $1,000 |  | $1,000 |  | $1,000 |  | $1,000
 |  |  | SUBTOTAL: |  | $6,000 |  | $4,000 |  | $9,000 |  | $5,000
 |  |  | CONTINGENCY (20%): |  | $2,000 |  | $1,000 |  | $2,000 |  | $1,000
 |  |  | TOTAL: |  | $10,000 |  | $5,000 |  | $20,000 |  | $6,000
Link
Notes: -No Site Specific Surveys
-Do not include environmental permits, mitigation, fees and other associated costs such as geotechnical analysis

## Slide 36: Standard Drawings
Link

## Slide 37: Contract Ready Documents

## Slide 38: Consultant Lessons Learned
Need Crash Records
Location of Crashes
District Preferences
Involvement of Agencies / Divisions
Notes: Just joking – don’t allow farmer’s markets near intersections – seems like this was a recurring them at many of the identified intersections.

## Slide 39: Current Project Status
9 of 50 have been advanced to some degree
  1 Completed
  2 Under Construction
  1 In Right of Way/Utilities
  5 In Design
  PCR for Current Projects = 70.1
  Projected Total Costs = $2 million

## Slide 40: Current Issues and Limitations
Unable to Separate Collision Data
Crash Locations not always accurate
Local Road Data
Major/Minor Approaches are currently being assumed
Updates are Yearly
Local Knowledge

## Slide 41: Additional Uses
Roundabout analysis
Help with vehicle routing (Superload)
ADA inventory (Ramp Data in progress)
Pavement inventory
Signal timing database
Expanding Existing HIS Data

## Slide 42: Questions