This is a rough set of instructions for manually creating a Bluetooth

Cellphone connection using Tmobile on a Carlson Explorer I & II or a

Juniper Allegro that is using Socket Bluetooth from the Carlson Knowledge Base.

http://update.carlsonsw.com/kbase_main.php?action=main_page&cat=105

!!!WARNING!!!  You will need an UNLIMITED data plan on your Cellphone

before using your cellphone to connect to the Internet for using it with

the GPS Reference networks !!!

1) Open the Start Menu by tapping the very bottom edge of the Screen -or-

hold the CTRL key and tap the ESC Key

a.  Tap the blue "B" Icon in the bottom right corner

b.  make sure the Bluetooth is turned on

c.  Tap the "B" icon / tap Advanced Features / tap My Bluetooth Devices

d.  Make sure the box is checked for Connectable

e.  Tap comms tab and make sure the Box is checked for Bluetooth Phone

f.   Tap OK in the upper right to accept the changes

2) Tap the BT Icon / tap Get Connected / tap Next and follow the prompts to

select the Bluetooth Phone and Bond to it

3) Start Menu / Settings / Network and Dialup / tap the Connection

pull-down in the Upper Left / tap New / type in TMOBILE for the name / tap

Next

4) Pick Bluetooth Phone from the top of the Pulldown List / tap Next / for

the Phone Number enter in the code below then tap Finish to return to the

Network and Dialup window

*99#

5) Tap once on the "TMOBILE" icon we just created / tap Connections / tap

Properties

6a) tap Configure / set the Baud Rate in the upper left to "115200"

6b) tap the Call options tab = uncheck the boxes for "Cancel call if not

connected" and "Wait for dial tone"

6c) Type in the code below into the "Insert Modem Commands" box

+cgdcont=1,,"internet2.voicestream.com"

then tap OK / tap OK again to return to the Network and Dialup window

!NOTE: This line of code is case sensitive and it needs to be entered in

exactly as shown above!

7) double-tap the "TMOBILE" icon

8) tap "Dial Properties" / tap Edit in bottom right / Enter just G in each

of the 3 boxes and hit the ENTER key on keyboard once all 3 boxes have just

the letter G in them / tap OK

!NOTE: if you tap the X in the upper right instead of hitting the Enter Key

the changes won't save

9) Leave the Username, Password and Domain blank

10) tap Connect

11)  It should go to a Status of "Connected" with the choice to Hide.  At

this point you should be connected to the Internet