## Slide 1: Intelligent Compaction
By: Adam Ross
KYTC Div. of Construction

## Slide 2: What is Intelligent Compaction??
What is IC?
How Intelligent is smashing things together?
Why we going to use IC?
What are you going to have to do?

## Slide 3: Proper compaction

## Slide 4: The “Smart” Roller
Positioning System
  GPS
  Laser
  Cell
Temperature Gauges (asphalt)
Accelerometer
Onboard Reporting System with display screen

## Slide 10: What it tells us
Where the roller went
What it did to the Soil, DGA, or Asphalt
Temperature of the Asphalt
Stiffness of the material

## Slide 13: Why use this stuff??
Test more area
Limit amount of extra rolling
Improved Density
Increased Productivity
Reduction of Highway Repair Costs
Continuous Record of Material Stiffness Values
Identification of Non-Compacted Areas
Improved Depth of Compaction

## Slide 16: KYTC and IC
Special Notes
5 projects in 2015
  2 Grade and Drain and Aggregate Base
  2 Asphalt only
  1 Soil, Ag. Base, and Asphalt
Specifications still govern acceptance

## Slide 17: Inspection
Test strip required to set pass count and “target” stiffness
Get the data and review it (VEDA)
Have your density tests surveyed to correlate to the IC value

## Slide 19: Lexington Workshops
April 14 at District Office
April 15 Equipment Demonstration Section office
http://www.intelligentcompaction.com/learn/workshops/current/2015-icdm-workshop-ky-01/

## Slide 20: Questions?