## Slide 1: Post Installation Pipe Inspection Training Course & Pipe Inspection Contractor Certification Program
Prepared for the
Kentucky Transportation Cabinet
by
Kean H. Ashurst Jr., P.E.
Kentucky Transportation Center

## Slide 2: Training Course
For KYTC personnel
Topics covered
  Inspection standards
  Types of inspections
  Inspection technology
  Inspection process
  Defects & distresses
  Inspection report requirements and review
  Pay deduction examples

## Slide 3: Training Course Highlights
Section 701
  Inspection of pipe
  Payment deduction tables
KM 64-114
  Equipment requirements
  Pipe inspection procedures
  Report requirements

## Slide 4: Training Course Highlights
Section 701.03.08
  Min. 250 LF of pipe and ADT > 1000
  100% of pipes under pavement
  50% of pipes not under pavement
    To be chosen by Section Engineer
    Priorities
      Culvert
      Storm sewer
      Outlet runs
    Entrance pipes chosen last to complete footage req.
    Must complete entire run – junction to junction

## Slide 5: Training Course Highlights
Section 701.03.08 Continued
  Rigid pipe deductions (installed pipe)
    Crack width > 0.1 inch = Remediate or Replace
  Flexible pipe deductions for deflection
    0% to 5.0% = 100% unit bid price
    5.1% to 7.5% = 75% unit bid price
    7.6% to 9.9% = 50% unit bid price
    10% or greater = Remove and replace
    All pipe with deflections between 5% and 10% require evaluation by engineer
    Special circumstances pipes with deflections greater than 10% may be allowed to remain in place
      public’s best interest, structural analysis, no pay

## Slide 6: Training Course Highlights
Section 701.03.08 Continued
    Deduction applied to whole stick of pipe
    Example: If max deflection is between 7.6% and 9.9% then that 20 foot stick is 50% of unit bid
  Cracking and Deflection…that’s not all
    Look for other distresses that indicate improper installation or damaged pipe
    Inspecting contractor should identify all distresses so you may make an informed decision

## Slide 7: Common Distresses

## Slide 8: Training Course Highlights
What you should be receiving from contractor
2 types of inspections = 2 types of reports
  Video Inspection Report
  Deflection Inspection Report
2 paper copies need to be provided by contractor
  1 to Section Engineer
  1 to Central Office
1 digital copy need to be provided by contractor
  Thumb drive
  DVD
  Portable Hard Drive

## Slide 9: Video Inspection Summary Report – TC 64-766

## Slide 10: Individual Pipe Video Inspection Report – TC 64-765

## Slide 11: Deflection Inspection Summary Report – TC 64-768

## Slide 12: Individual Pipe Deflection Inspection Report – TC 64-767

## Slide 13: Example Profiles

## Slide 14: Example Profiles

## Slide 15: Are deflection results in the ballpark?
Expected Dia. = Nominal or Mean or Base Dia.

## Slide 16: Check Deflections from Video
 | Meas. | Notes
 | (pts) | 
1 | 196.50 | Vert.
2 | 208.03 | 
3 | 216.27 | 
4 | 225.77 | 
5 | 233.94 | Horz.
6 | 228.35 | 
7 | 217.67 | 
8 | 201.03 | 
Mean | 215.95 | 
Vert. Def. | -9.0 % | 
Horz. Def. | 8.3 % | 
1
5
Notes: Use a joint in the video

## Slide 17: Contractor Certification Program
Purpose: ensure the inspecting contractor can adequately identify and measure distresses and submit the appropriate documentation
Video inspection
Deflection inspection
Report requirements and submittal

## Slide 18: Contractor Certification Program
1. Video inspection
  Identify and catalog all distresses
  Catalog all joint locations
  Correctly determine longitudinal locations of all distresses
  Determine widths of cracks and joint separations

## Slide 19: Contractor Certification Program
2. Laser deflection measurement
  Identify maximum deflections
  Locations of all deflections
3. Inspection reports
  Properly fill out all summary TC reports
  Inclusion of video distress catalog software report
  Inclusion of deflection software report

## Slide 20: Contractor Certification Program
How?...we set up a test track
3 pipe types
  HDPE
  CMP
  RCP
In-situ like distressed conditions
Modular w/ short sticks & RCP on skates so we can change the course

## Slide 24: Contractor Certification Program
Contractor given 8 hours to perform inspections
7 business days to submit complete report
7 business days for KTC review and grade
  Deflection results compared to our hand measurements
If contractor passes they will be issued a letter stating such and must be kept on-hand at all times

## Slide 25: Thank You
More dates for training class will be announced shortly
If you have specific examples or questions please call anytime…we are here to help!!!
Kean H. Ashurst Jr., P.E.
Kentucky Transportation Center
University of Kentucky
176 Raymond Building
Lexington, KY 40506
(859) 257-7319
kean.ashurst@uky.edu