## Slide 1: MAP 21 Performance Measures for Pavements and Bridges
Jon Wilcoxson
Division of Maintenance

## Slide 2: Moving Ahead for Progress in the 21st Century (MAP-21)
Federal Surface Transportation Funding Bill
Signed into Law July 2012
Establishes a Performance-Based Program for Highways

## Slide 3: Performance Based Program
Focus on National Transportation Goals
Increase Accountability and Transparency
Improve Investment Decision-making

## Slide 4: Focus Areas for Performance
Safety
Infrastructure Condition
Congestion Reduction
System Reliability
Freight Movement and Economic Vitality
Environmental Sustainability
Reduced Project Delivery Delays

## Slide 5: Focus Areas for Performance
Safety
Infrastructure Condition
Congestion Reduction
System Reliability
Freight Movement and Economic Vitality
Environmental Sustainability
Reduced Project Delivery Delays

## Slide 6: Infrastructure
Pavement
Bridges
Guardrail
Signs
Signals
Striping
Pipes
Etc.

## Slide 7: Infrastructure
Pavement
Bridges
Guardrail
Signs
Signals
Striping
Pipes
Etc.

## Slide 8: Notice of Proposed Rulemaking (NPRM) for Pavement and Bridge Conditions
Published January 5, 2015
Establishes Required Performance Measures and Targets for National Highway System
Comment Period through May 8, 2015

## Slide 9: Pavement Condition Measures
INTERSTATES | NON-INTERSTATE NHS
% of “Good” Pavements | % of “Good” Pavements
% of “Poor” Pavements | % of “Poor” Pavements

## Slide 10: Required Metrics
Smoothness (IRI)
Cracking
Rutting (Asphalt)
Faulting (Concrete)

## Slide 11: How are “Good” and “Poor” Defined?
 | Good | Fair | Poor
IRI (inches/mile) | <95 | 95-170 | >170
Cracking (%) | <5% | 5% - 10% | >10%
Rutting (inches) | <0.20 | 0.20 – 0.40 | >0.40
Faulting (inches) | <0.05 | 0.05 – 0.15 | >0.15

## Slide 12: Determining Pavement Condition
Metric Rating Results | Overall Section Rating
All three metrics rated “Good” | Good
More than 2 metrics rated “Poor” | Poor
All other combinations | Fair

## Slide 13: Required Threshold and Penalties
No more than 5% of Interstate Pavements allowed in Poor Condition
If target is not attained for two consecutive years, state must obligate funds to improve the measure.

## Slide 14: Bridge Condition Measures
National Highway System
% of Bridges in “Good” Condition
% of Bridges in “Poor” Condition
% By Deck Area

## Slide 16: Determining Bridge Condition
Metric Rating Results | Overall Section Rating
All three metrics rated “Good” | Good
ANY Metric Rated “Poor” | Poor
All other combinations | Fair

## Slide 17: Required Threshold and Penalties
No more than 10% of NHS Bridge Deck Area allowed in Poor Condition
If target is not attained for three consecutive years, state must obligate funds to improve the measure.

## Slide 18: Potential Concerns
Extremely High Threshold for Poor Pavements on Interstate

## Slide 19
 | Good | Fair | Poor
IRI (inches/mile) | <95 | 95-170 | >170
Cracking (%) | <5% | 5% - 10% | >10%
Rutting (inches) | <0.20 | 0.20 – 0.40 | >0.40
Faulting (inches) | <0.05 | 0.05 – 0.15 | >0.15

## Slide 20: Potential Concerns
Extremely High Threshold for Poor Pavements on Interstate
Missing Data is Considered Poor by Default

## Slide 21: Potential Concerns
Extremely High Threshold for Poor Pavements on Interstate
Missing Pavement Data is Considered Poor by Default
Forces Bridge Program to Focus on NHS
Deck Area emphasis may hurt rural areas
Replacement vs. Preservation

## Slide 22: Possible KYTC-Specific Measures
Pavements
% Poor Pavements (by KYTC Definition, NHS and non-NHS)
% Good Pavements (by KYTC Definition, NHS and non-NHS)
Average Remaining Service Life (NHS and non-NHS)
Bridges
# of Substandard Bridges on State Routes
# of Structurally Deficient Bridges (entire system)
% Structurally Deficient Deck Area (entire system)

## Slide 23: Questions/Comments
Comment period open until May 8, 2015