## Slide 1: Pipe iNSTALLATION
2013 Section Engineer’s Meeting

## Slide 2: Before Installation Begins
Correct Type, Gauge, and Coating (Standard Drawings)
  Based on Pipe Diameter, Fill Height & Soil pH
Obtain copy of Manufacturer’s Handling and Installation procedures
Pipe Condition
  Defects to look for are different for each type of pipe (RCP, CMP, PVC…etc.)

## Slide 3: Standard Drawing RDI-035-01

## Slide 6: Preparing the Trench
Check Staking
  Correct Station
  Inlet/Outlet Elevations
  Ensure proper grade.
Pipe Pads/Trench Condition
Excavation
Pipe Undercut if Rock or Soft Foundation
  Price is in Spec Book

## Slide 8: Laying the Pipe
Joints
  Construct per Spec depending on Type of Pipe
  54” and greater must be wrapped with Type IV Fabric – 3’ min width
Bedding and Fabric
  Use No. 8 or 9-M aggregate for bedding
  Excavate a cradle for pipe and check with template
  Use Type IV Fabric when backfill and surrounding conditions are different gradations, at $2 / sq yd

## Slide 9: Backfill
Backfill and Compaction
  Granular Backfill in Trench
  Flowable Fill –if under existing road or within one pipe diameter of subgrade
  Construction Loads – 48 Inches min depth needed
  Monitor Pipe During Construction
“Too much emphasis cannot be placed on the necessity of adequate compaction of backfill. Faulty compaction has led to more trouble with pipe installations, flexible and rigid, than all other factors combined!” NCSPA

## Slide 11: Other Requirments
Safety
  OSHA Standards
Proper Erosion Control

## Slide 12: 2012 NEW SPECS
Pipeline Video Inspection
(> 250 LF of Pipe and ADT > 1,000)
  Conduct camera/video inspections in accordance with KM 64-114 on 100 percent of the pipes that are located under the road and 50 percent of the pipes that are not under the road.
  Schedule the inspections no sooner than 30 days after completing the installation and completion of earthwork to within 1 foot of the finished subgrade.

## Slide 13: Pipe Inspection Results
Crack Testing for Rigid Pipe
  < or = 0.1 inch – 100% Pay
  > 0.1 inch - Remediate or Replace
Deflection Testing for Flexible Pipe
  0.0 to 5% - 100% Pay
  5.1 to 7.5% - 75% Pay
  7.6 to 9.9% - 50% Pay
  10% or greater – Remove and Replace
  Note: Structural Analysis to be provided if over 5%