## Slide 1: The Brent Spence Companion Bridge Because One Bridge Wasn’t Enough September 10, 2026

## Slide 2: PRESENTERS
Craig Klusman
Deputy Design Manager
Talya Caudill
KYTC Construction Lead
Will Banik
WKJV River Crossing
Project Manager

## Slide 3: AGENDA
Background & Project Overview
Challenges
Notes: Looks like a short agenda but don't worry – we have LOTS to talk about :)

## Slide 4: BACKGROUND & PROJECT OVERVIEW

## Slide 5
Notes: Talya
Photos from the construction of the Brent Spence Bridge. Built in 1963. Original cost $2.74 Million
It is a double decker cantilever truss carrying 71 and 75 across the Ohio river between Kentucky and Ohio.

## Slide 6
Notes: Talya

## Slide 7
Before: Three 12-feet lanes & 5-feet shoulders
Now: Four
11-feet lanes &
1-foot shoulders
Notes: BSB was built to carry only 3-12’ lanes and 5’ shoulders on both decks - 80k veh/day
Quickly Re-striped in 1985 to carry 4-11’ lanes with 1’ shoulders. Is now carrying more than double the volume.

## Slide 8: BACKGROUND
Brent Spence Bridge
Brent Spence Bridge
The Brent Spence Bridge Corridor Project represents one of the nation’s most significant transportation transformations.​
The BSB Carries…
  Nearly 3% Of The Nation’s GDP
  $1+ Billion Daily in Freight
The BSB Connects To….. The Port Of Cincinnati
The BSB Connects To…. CVG
  7th largest cargo airport in North America (2025)
  Home to dual cargo hubs: Amazon Air Hub & DHL Express Global Superhub
The Project will:​
  Address one of the most severe traffic bottlenecks in the country​
  Reshape how Ohio and Kentucky move, connect and grow​
Notes: I-75 – Miami Lakes, FL to the canadian border – 1,786 miles
I-71 – Louisville to Cleveland - 345 miles

## Slide 9: CORRIDOR OVERVIEW
8-mile corridor from Dixie Highway (KY) to the Western Hills Viaduct (OH)
  5 miles of I-71/I-75 in KY
  3 miles of I-75 in OH
Widen I-71/I-75
Rebuild all overpass bridges and interchanges
Build a collector-distributor system between Covington and Cincinnati
Update the existing Brent Spence Bridge
  Rehabilitate the structure
  3 lanes on each deck
  Inside/outside shoulders
  Carry local traffic
Build new companion bridge
  West of existing Brent Spence Bridge
  5 lanes on each deck
  Carry interstate traffic
Western Hills Viaduct
Ezzard Charles Dr
W 5th St
Pike St
W 12th St
OHIO
KENTUCKY
Cincinnati
Covington
NORTH
127
42
127
42
Notes: The overall corridor includes widening just under 8 miles of I-71/I-75 from south of Dixie Highway in Kentucky to the Western Hills Viaduct in Ohio and rebuilding all bridges and interchanges. A collector-distributor system will be added between 12th Street in Kentucky and Ezzard Charles Drive in Ohio. A collector-distributor system is a network of roads alongside a highway that “collects” traffic exiting from a highway and “distributes” it to local roadways. It also “collects” traffic from local roadways and “distributes” it onto the highway.
The existing double-decker Brent Spence bridge will be rehabilitated and reconfigured to reduce the number of lanes on each deck from four to three and provide inside and outside shoulders. The existing bridge will carry local traffic as part of the proposed collector-distributor roadway system. Between Ohio and Kentucky, the project will build a new double decker companion bridge with five lanes on each deck west of the existing BSB. The new bridge will carry through (interstate) traffic across the Ohio River.

## Slide 10: WHAT WE'RE BUILDING NOW
New Companion Bridge and One Mile of Approaches
Two-tier, independent deck cable-stayed bridge carrying five lanes of northbound (upper level) and southbound (lower level) interstate traffic
  Existing Brent Spence Bridge will carry local traffic
One-mile approach to the new bridge in Ohio and in Kentucky
Constructing a C-D roadway system between West 12th Street/Martin Luther King (MLK) Jr. Boulevard in Kentucky to Linn Street in Ohio
Extending frontage roads connecting Pike Street to West 4th Street and West 5th in Kentucky
New pedestrian and bicycle paths and aesthetic improvements for walkable, urban connectivity
2.25 miles
Kentucky +
Companion Bridge + Ohio
2026-2033
Current Phase Construction Timeline
90+ firms
Design, Construction & Utility Work
$4.05B
Cost of First Construction Phase

## Slide 11: PROJECT TEAM
Bi-State Management Team
Design Build
Team
(DBT)
Lead Designer
Construction
Engineering
& Inspection
(CEI)
State Cost
Estimator
(SCE)
Independent
Cost
Estimator
(ICE)
Quality
Assurance
Manager
(QAM)
Contract
Consultant
Oversight
Manager
(CCOM)
Notes: A PROJECT LIKE THIS NEEDS 100S, 1000S OF PEOPLE, ORGANIZATIONS DISCIPLINES AND PERSONALITIES TO WORK TOGETHER.

## Slide 12
Design-Build
Progressive
Design-Build
CMGC & CMAR
Owner
Design-Build Contractor (GC + Designer)
Owner + Independent Cost Estimator (ICE)
Design-Build Contractor (GC + Designer)
Owner + Independent Cost Estimator (ICE)
Designer
Contractor
Owner
Designer
Contractor
Design-
Bid-Build
Preconstruction
Construction
DELIVERY METHODS
COMPARISON
Notes: DBB – the phase between design and construction can be infinite.
DB – RFQ –> short list -> RFP @ about 35% design. No need for an independent cost estimator because there is a price component to the RFP process meaning competition. limits innovation as the DBT is coming in later. Pricing is fixed at contract signing so likely lots of built in risk.
PDB – DBT is on board prior to environmental clearance, R/W clearance, etc so they are able to impact those decisions. A budget is set early but the pricing (GMP) is negotiated at a much later phase (often 60 or 90% plans)
CMGC – similar to PDB but there are separate contracts with the designer and the contractor.
Both CMGC and PDB typically have an off-ramp option which allows the owner to terminate the agreement if a price cannot be negotiated. It forces pricing transparency and allows the owner to take ownership of the plans and switch to a traditional DBB to hopefully provide some competition and allow the owner to achieve a more reasonable price. They also both
One of the key takeaway or advantages of alternative delivery = risk sharing is typically less costly than risk shedding.

## Slide 13: CHALLENGES
Notes: We want to talk about some of the challenges we've faced and/or are currently facing and the opportunities that came from those challenges OR the opportunities that the PDB model has provided us.

## Slide 14: Challenge: Capacity
Brent Spence Bridge Design Volume
Current Volume
80,000 veh/day
160,000+ veh/day
Companion Bridge
Opportunity:
Notes: CRAIG
To start at the beginning, the first obvious challenge is the current capacity of the bridge. Simply demolishing the existing bridge and building something twice the size wasn't feasible.
Companion bridge will accommodate 5 lanes in each direction for mainline I-71/75
Existing bridge will be reconfigured for 3 lanes in each direction for local connections to downtown Covington and Cincinnati.

## Slide 15: Challenge: Bridge Type Selection Site Limitations - USCG Requirements
  Ohio River
  Congested site with many bridges
  33° bend in river
  Vessel traffic
Notes: CRAIG
So we know we're building a companion bridge. Next challenge – choosing a bridge type. The site conditions played a huge role in the selection of the bridge type.
The Ohio river is a vital corridor for commerce, transportation, and recreation.
The vessel traffic passing beneath the bridge predominantly consists of flotillas of barges propelled by tugboats. Vessels included in the study also comprised errant vessels and drifting empty barges.

## Slide 16: Challenge: Bridge Type Selection Site Limitations - USCG Requirements
Navigation channel developed with Army Corps of Engineers
Opportunity – Open and wider channel
Pylons designed to resist the associated collision forces from the vessel traffic.
Notes: CRAIG
Coast Guard Requirements: 1) Substructures outside of existing bridge, 2) Yellow window shown, 3) Vertical clearance
Opportunity: 960-ft clear main span with pier just off of Kentucky bank
Pylons designed for vessel collision in accordance with AASHTO LRFD and Guide Specs: 1) Errant vessel and 2) drifting empty barge (travelling at water current speed).
Next: Now, structure type selection...

## Slide 17: Challenge: Bridge Type Selection
PRELIMINARY
ARCH CONCEPT
PRELIMINARY
CABLE-STAY CONCEPT
Cable-Stay Option
(Preliminary)
Arch
Option
(Preliminary)
Notes: WILL
Not only did the site limitations play a large role in the bridge selection but the PDB model also allowed the opportunity of early contractor involvement. The WKDBT actually introduced the idea of the cable stayed independent deck and vertical pylons.
The design build team’s Initial focus once engaged was to evaluate the bridge types not only for cost, but for constructability and durability as well; in support of the project goal want to ensure the structure built requires relatively minimal maintenance and is highly durable to serve the needs of the community and the nation for decades to come. PDB model allowed DBT to propose a unique cable-stayed solution in which each bridge deck is supported independently on separate sets of stay cables – we’ll touch on some of the key factors for each type that influenced the decision making.
ENVIRONMENTAL COMMITMENT
-25-ft vertical clearance between deck
-Structure height between 300-ft min and 420-ft max
-Pier placement for navigation

## Slide 18: Challenge – Meeting USCG Requirements
Notes: WILL & CRAIG
Balanced and Symmetric Spans: Sidespans at about 40%-45% of mainspan for efficient structure design (42% sweet-spot). Minimize uplift potential at transition piers with ballast.. BSB at 45%
BSCB has 40-ft ballast zone at ends.

## Slide 19: Opportunity: Unique Bridge Type
Benefits
All steel I-girder sections in superstructure – less fabrication time and fit-up risk
No enclosed steel sections to inspect
Freestanding pylons without cross struts – provides visually open structure
More natural light on the lower deck
The bridge will be unique in that each deck level is supported by its own set of stay-cables that are independent.
Notes: CRAIG
A unique bridge type! Truly one of a kind – touch on other aspects of the bridge that make it unique
Double deck with independently supported decks, like two bridges supported on each pylon.

## Slide 20: Unique Structure Type Challenges
Wind
Independent decks with parallel cables – sensitive to wake induced galloping
Stay Cables
Impact on edge girder geometry
Corrosion Protection for Deck
Epoxy Coated Deck Post-Tensioning
Stainless Steel Rebar
Notes: CRAIG
But with a unique bridge type comes it's own set of challenges...
Wind – Wake Galloping and flutter due to adjacent cables.
Corrosion Protection for Deck included epoxy coated deck post-tensioning strands, and stainless steel rebar.

## Slide 21
Wind Tunnel Testing of Scaled Prototype Models to confirm aerodynamic stability and determine design loading
Challenge: Wind
Notes: CRAIG
Sectional model for aerodynamic stability of cross-section
Full aeroelastic model to verify aerodynamic stability and to provide wind loads to design structure.
Cable vibration study to make sure cables don’t have movement under wind, run with vehicles/ w/o existing bridges,
Summary – No concerns or significant changes to design from the wind study. Independent decks proved out to be stable.

## Slide 22
Opportunity: Donation of the Model
Notes: TALYA
ODOT was able to donate the model to the Cincinnati Museum Center

## Slide 23: Challenge: Stay Cables
Semi-Harp Arrangement
Parallel stay cables spaced at 5’-0”
Designed for Cable Loss and Cable Replacement scenarios
176
Total Stay Cables on the bridge
96 Upper deck / 80 Lower deck
Notes: CRAIG
Regularly spaced on the lower deck at 45’-0” or 30’-0”
On the upper deck, spacing varies as lower deck cable passes by upper deck at varying angles
2 additional sets of cables on the upper deck

## Slide 24: Challenge: Stay Cables Impact on Edge Girder Geometry
Stay Cables are parallel with roadway and edge girders
Solution – Deviated Edge Girder
Notes: CRAIG
Stay cables and edge girders parallel to deck
Stay cables need to be continuous w/o bearings at pylons..
Hence the deviated edge girders.

## Slide 25: Challenge: Deck Corrosion Protection
Deck Post Tensioning Mockup
Opportunity:
Notes: TALYA
KYTC recommended epoxy coating the strands – this has never been done before in a bonded tendon application in a bridge deck. We’re on the cutting edge of this – PTI is really just now talking about this.

## Slide 26: Challenge: ACTUALLY BUILDING THE THING!
Notes: WILL

## Slide 27: Challenge: Site Access/Limitations during Construction
Notes: WILL
Site access/limitations and the fluctuation of the River; designing temporary works to accommodate typical river conditions and mitigate delays to the schedule

## Slide 28: Challenge: Site Access/Limitations during Construction
Custom Engineered Solutions
Opportunity:
Notes: WILL

## Slide 29: Challenge: Craft Labor Force
Notes: WILL
craft labor demand, competition with other projects in the area for qualified craft

## Slide 30: Challenge: Craft Labor Force
Outreach and Engagement
Opportunity:
Notes: WILL
BWE team have conducted dozens of outreach events to engage sub suppliers
ACI construction career days, She Builds, etc.
Coordination with local trade unions to inform them of needs

## Slide 31: Challenge: Project Duration
Notes: WILL
This is a LONG project. Substantial completion is scheduled for 2033! Material prices fluctuate, cost of fuel fluctuates – and usually in the positive direction. Accurately capturing that escalation is difficult especially in a way that is fair to both owner and contractor. Fortunately, with the PDB model we were able to [insert something here that sounds good and doesn’t talk too much about risk and $$]

## Slide 32: Challenge: Project Duration
Cool 4D Scheduling Tools!
Opportunity:
Notes: WILL
This is a LONG project. Substantial completion is scheduled for 2033! Material prices fluctuate, cost of fuel fluctuates – and usually in the positive direction. Accurately capturing that escalation is difficult especially in a way that is fair to both owner and contractor. Fortunately, with the PDB model we were able to [insert something here that sounds good and doesn’t talk too much about risk and $$]
Staff attrition / turnover, burnout, etc.

## Slide 33
Notes: This presentation covered a very select few of the challenges this project has encountered so far. Here’s a cool 4D schedule that completely breezes past all of those challenges and makes this project look super easy.

## Slide 34: THANK YOU!
INVESTING IN LOCAL COMMUNITIES. GROWING AMERICA’S ECONOMY.
brentspencebridgecorridor.com

## Slide 35: Challenge – Hydraulic Requirements
The bridge is in a Flood Emergency Management Agency (FEMA) floodway of the Ohio River
1D hydraulic model – Impact on Regulatory and 100-year Floodplain
2D hydrodynamic models were developed to compute scour depths
3D computational fluid dynamic analyses were undertaken to study the effects of scour interaction between the two bridges

## Slide 36: Challenge – Hydraulic Requirements
Zero-rise condition met within the regulatory and 100-year floodway
The companion bridge foundations are designed to accommodate the anticipated scour depths of approximately 40 to 50 feet
Notes: 3D – overlapping scour holes