## Slide 1
Thinking Beyond the Intersection and Project Limits
Austin Hart, KYTC District 1
Brian Aldridge, Stantec

## Slide 2
Agenda
Project History
Before and After Construction
Lessons Learned

## Slide 5
West of the Interchange
James Sanders
Kentucky
Oaks
Mall
~600’

## Slide 6
East of the Interchange
Coleman Road
~620’
Perkins Creek

## Slide 7
At the Interchange
~100’

## Slide 8
2012 Scoping Study
US 60 Scoping Study recommended a Double Crossover Diamond (DCD) interchange
2022 Design Year (10-year)

## Slide 10
Preliminary Concept
Proposed Beneath I-24
11’
11’
11’
11’
11’
11’
11’
10’
Approximately 100’
20’

## Slide 11
James Sanders Boulevard
James Sanders

## Slide 12
James Sanders
Boulevard
Dual right turn lanes (original configuration)

## Slide 13
James Sanders
Boulevard
Single free flow right with no changes to James Sanders

## Slide 14
James Sanders
Boulevard
Single free flow right with proposed access management

## Slide 15
James Sanders Boulevard
James Sanders

## Slide 16
Coleman Road
Coleman Road

## Slide 17
Construction

## Slide 18
Public & Business Reaction
"It was kind of odd at first, because you're switching sides, but I'm used to it," said Phillip Barnett. "I love it.“
"I can remember trying to get through the traffic prior to it being built, and it seems like this is a whole lot speedier. It's faster," Barnett said.
Source: www.wpsdlocal6.com

## Slide 19
2017 2024
Freddy’s
Starbucks
QDOBA
Jimmy John’s
Cheddars /
Chuy’s
Pizza Hut

## Slide 20
Daily Traffic (in Vehicles per Day)
+15%

## Slide 21
Route | Direction | Location | Average Hourly Speed (mph) |  |  |  |  | 
 |  |  | 2017 | 2018 | CONSTRUCTION | 2021 | 2022 | 2023
US 60 | EB | West of interchange | 22.5 | 23.0 |  | 23.3 | 24.4 | 21.9
 |  | Through interchange | 20.0 | 20.1 |  | 16.8 | 16.5 | 16.6
 |  | East of interchange | 30.3 | 30.8 |  | 25.5 | 28.5 | 29.8
 | WB | East of interchange | 30.8 | 30.8 |  | 25.7 | 27.1 | 27.9
 |  | Through interchange | 21.5 | 21.8 |  | 14.6 | 14.9 | 14.1
 |  | West of interchange | 24.8 | 25.6 |  | 20.3 | 21.0 | 20.5
Travel Speeds

## Slide 22
Travel Speeds (by Design)

## Slide 23
Crash Experience
2016 - 2018
  437 Crashes
  54 Injury (12.4%)
2023 - 2025
  374 Crashes
  45 Injury (12.0%)
  -15% reduction overall
  -30% at ramps

## Slide 24
Crosswalk Request
Coleman Road
Perkins Creek

## Slide 25
Restaurant
Restaurant
Restaurant
Restaurant
Hotel
Hotel

## Slide 26
Coleman Road: 2021-2025
140
Reported Collisions
19
injury-involved collisions
29
total reported injuries
121
property-damage collisions
3
commercial-vehicle collisions
0
fatalities
4
Notes: [Sources]
- User-provided crash-history document, Coleman Road summary screenshot and map screenshot.
- Derived share: 19 injury-involved collisions / 140 total collisions = 13.6%.
[/Sources]

## Slide 27
James Sanders: 2021-2025
215
Reported Collisions
19
injury-involved collisions
20
total reported injuries
196
property-damage collisions
3
commercial-vehicle collisions
0
fatalities
Notes: [Sources]
- User-provided crash-history document, James Sanders Boulevard summary screenshot and map screenshot.
- Derived share: 19 injury-involved collisions / 215 total collisions = 8.8%.
[/Sources]

## Slide 28
James Sanders South of US 60
City Streets - Pecan Drive, Village Square, Bell Aire Drive
New Business –Restaurants, Dr. Offices, Home Improvement Stores
Commuter Traffic avoiding Interstate 24
Cheddars / Chuy’s
Doc. Office
Academy (2017)
Coleman Road
Bell Aire Dr
Village Square

## Slide 29
Conclusions
Consider all available Data
Design Year: 5 -10 years versus 25 years
Considering Traffic Generators
Permit Guidance to City / County Planners
How soon do we revisit the same area?

## Slide 30
Questions?