## Slide 1
Where the Sidewalk Ends – Filling in the Gaps
Deanna Mills, PE – KYTC – Traffic Safety Branch
Daniel Wyatt, PE – KYTC – District 5
Jennifer Hardwick, PE, RSP1 – HMB Professional Engineers
Ill.: Shel Silverstein

## Slide 2: Background: VRU RSAs
Over 192 RSA locations in 2023 & 2024 – all that involve a serious injury or fatality.

## Slide 3: Background: Data Driven Solutions
65% of pedestrian deaths occurred in locations without a sidewalk present. – FHWA
The likelihood of a pedestrian crash along roadways with no sidewalk is 1.67 greater. – Florida DOT
Installing sidewalk has a 0.598 crash modification factor for vehicle/pedestrian collisions. CMF Clearinghouse

## Slide 4: Identifying the Gaps
469 gaps identified
Over 117 miles of sidewalk
43.7% of segments were on the HIN

## Slide 5: SCI Methodology: Washington D.C. Method
SCI – Sidewalk Constructability Index
  20% - Transportation Need
  20% - High Injury Network
  20% - Roadway Functional Classification
  10% - Proximity to Schools
  10% - Proximity to Parks, Trailheads, & Rec Centers
  10% - Proximity to Bus Stops
  10% - Proximity to Transit Stations
https://sidewalkgap.ddot.dc.gov/

## Slide 6: SCI Methodology: Louisville Method
22.2 % - Transportation Need
  Transportation Insecurity Percentile > 66.6% = 10 Points
  Transportation Insecurity Percentile between 33.3 and 66.6% = 5 Points
  Transportation Insecurity Percentile below 33.3% = 1 Point
22.2% - High Injury Network
  On HIN = 10 Points
  Off HIN = 1 Point
22.2% - Roadway Function
  Principal Arterial = 10 Points
  Minor Arterial = 7 Points

## Slide 7: SCI Methodology: Louisville Method
11.1 % - Proximity to Schools
  Less than 1/8 Mile to School = 10 Points
  Between 1/8 and 1/4 Mile = 7 Points
  Between 1/4 Mile and 1/2 Mile = 4 Points
  Over 1/2 Mile = 1 Point
11.1% - Proximity to Bus Stops
  Less than 1/8 Mile to School = 10 Points
  Between 1/8 and 1/4 Mile = 7 Points
  Between 1/4 Mile and 1/2 Mile = 4 Points
  Over 1/2 Mile = 1 Point

## Slide 8: SCI Methodology – Louisville Method
11.1 % - Proximity to Shared Use Paths, Parks, and Rec Centers
  Based on the lowest distance of the 3
    Less than 1/8 Mile to School = 10 Points
    Between 1/8 and 1/4 Mile = 7 Points
    Between 1/4 Mile and 1/2 Mile = 4 Points
    Over 1/2 Mile = 1 Point

## Slide 9: SCI – Top Scoring Segments

## Slide 10
Constructable Projects
YOU ARE HERE
How do we get there from here?
469 Identified Sidewalk Gaps

## Slide 11
How do we get there from here?
Step 1
Develop Strategy
Step 4
Select Segments
Step 3
Sort Data
Step 2
Review Segments

## Slide 12
Step 1: Develop Strategy
Objective:
  Develop construction plans for sidewalk gaps
Information provided:
  Daniel’s list of prioritized sidewalk gaps in Jefferson County
  KMZ of sidewalk gap locations
HMB tasks:
  Perform high-level review of top 1/3 sidewalk gaps
  Assign difficulty rating to each gap
  Share results with team
Team task:
  Select group of sidewalk gaps for first round of project development

## Slide 13
Step 2: Review Segments
Right-of-Way
Utilities
Construction
High-level look at each individual sidewalk gap segment

## Slide 14
Step 3: Sort Data
Notes: Used this high-level review to assign a difficulty rating to each segment
we wanted it to be as quantifiable and reproducible as possible – consistency throughout entire process
Developed difficulty rating system based on DRUC to provide comprehensive evaluation
Went through each segment individually and gave it a rating

## Slide 15
Step 3: Sort Data
ID: |  | 348 |  | 
Name: |  | KY 2052 | MP 2.8 | Right
Weighted Score: |  | 8.67 |  | 
R: | Seems sufficient. May only cross a single property |  |  | 
U: | UP within ~6' of curb - could probably weave around. Other UG utilities unknown |  |  | 
C: | Already has curb and storm sewer, is just adding a short section of sidewalk |  |  | 
Difficulty: |  | Low |  | 
Comments: |  | Existing curb and storm sewer, flat, can likely avoid R&U impacts |  | 

## Slide 16
Step 3: Sort Data
ID: |  | 348 |  | 
Name: |  | KY 2052 | MP 2.8 | Right
Weighted Score: |  | 8.67 |  | 
R: | Seems sufficient. May only cross a single property |  |  | 
U: | UP within ~6' of curb - could probably weave around. Other UG utilities unknown |  |  | 
C: | Already has curb and storm sewer, is just adding a short section of sidewalk |  |  | 
Difficulty: |  | Low |  | 
Comments: |  | Existing curb and storm sewer, flat, can likely avoid R&U impacts |  | 
Existing Sidewalk

## Slide 17
Step 3: Sort Data
ID: |  | 348 |  | 
Name: |  | KY 2052 | MP 2.8 | Right
Weighted Score: |  | 8.67 |  | 
R: | Seems sufficient. May only cross a single property |  |  | 
U: | UP within ~6' of curb - could probably weave around. Other UG utilities unknown |  |  | 
C: | Already has curb and storm sewer, is just adding a short section of sidewalk |  |  | 
Difficulty: |  | Low |  | 
Comments: |  | Existing curb and storm sewer, flat, can likely avoid R&U impacts |  | 
Existing Sidewalk
Sidewalk Gap

## Slide 18
Step 3: Sort Data

## Slide 19
Step 3: Sort Data

## Slide 20
Step 4: Select Segments
ID: |  | 348 |  | 
Name: |  | KY 2052 | MP 2.8 | Right
Weighted Score: |  | 8.67 |  | 
R: | Seems sufficient. May only cross a single property |  |  | 
U: | UP within ~6' of curb - could probably weave around. Other UG utilities unknown |  |  | 
C: | Already has curb and storm sewer, is just adding a short section of sidewalk |  |  | 
Difficulty: |  | Low |  | 
Comments: |  | Existing curb and storm sewer, flat, can likely avoid R&U impacts |  | 
Review objective:
  Develop construction plans for sidewalk gaps
Review constructability evaluation results:
  Segment evaluation spreadsheet
  Segment KMZ
Select segments for first round of development:
  US 31W from Crums Lane to Bernheim Lane
  US 31W from Bernheim Lane to Lee Street
  US 31W at Ashby Lane / Valley Station Road

## Slide 21
Step 4: Select Segments
ID: |  | 348 |  | 
Name: |  | KY 2052 | MP 2.8 | Right
Weighted Score: |  | 8.67 |  | 
R: | Seems sufficient. May only cross a single property |  |  | 
U: | UP within ~6' of curb - could probably weave around. Other UG utilities unknown |  |  | 
C: | Already has curb and storm sewer, is just adding a short section of sidewalk |  |  | 
Difficulty: |  | Low |  | 
Comments: |  | Existing curb and storm sewer, flat, can likely avoid R&U impacts |  | 

## Slide 22
ID: |  | 348 |  | 
Name: |  | KY 2052 | MP 2.8 | Right
Weighted Score: |  | 8.67 |  | 
R: | Seems sufficient. May only cross a single property |  |  | 
U: | UP within ~6' of curb - could probably weave around. Other UG utilities unknown |  |  | 
C: | Already has curb and storm sewer, is just adding a short section of sidewalk |  |  | 
Difficulty: |  | Low |  | 
Comments: |  | Existing curb and storm sewer, flat, can likely avoid R&U impacts |  | 
Daniel Wyatt, PE – KYTC – District 5
Deanna Mills, PE – KYTC – Traffic Safety Branch
Jennifer Hardwick, PE, RSP1 – HMB Professional Engineers
Where the Sidewalk Ends – Filling in the Gaps