## Slide 1: Highway Safety Manual Implementation
Eric Green, PhD

## Slide 2: Kentucky’s Road to Implementing the HSM
Traditional approach
Known issues
Implementation of the HSM
Obstacles
Future improvements

## Slide 3: Traditional Approach
Critical Rate

## Slide 4: Critical Rate Analysis
Traditional way to quantify safety
Compare a section of road to an average section of road of a similar type
Compare the average rate to that of the critical rate (incorporates a 99.5% confidence)
Produces a Critical Rate Factor

## Slide 5: Critical Rate Factor
Ratio of Actual Rate over Critical Rate
CRFs over 1 are more “dangerous” than the average section
Typically sorted descending
Prioritization lists can be generated from the top X percentage
Also used in conjunction with planning metrics to rate all HPMS segments

## Slide 6: Known Issues

## Slide 7: Known Issues
Crash accuracy
Regression to the mean/randomness
Relation between crashes and AADT

## Slide 8: Limits of Critical Rate Analysis
Uses only collisions with county, route, mile point – other collisions excluded
Uses cookie cutter lengths to find sections - it doesn’t find the best section
Collision reports are not correct all the time – read them carefully
Sites with low AADTs tend to move to the top
No accounting for sites with zero crashes
Crash rates may be misleading

## Slide 9: Regression To The Mean
Sir Francis Galton, 1887
  Sweet pea seed size in successive generations
Mean
Federal Highway Administration
U.S. Department of Transportation

## Slide 10: What Did We Learn?
Crashes and AADT are not necessarily linearly related
Crashes are random events
Naïve before and after analysis can be misleading
Location data can be incorrect
Crash codes can be incorrect

## Slide 11: Kentucky Roadway
AADT = 15,000
Crashes (5 years) = 50
Crash Rate = 179
Length = 1.0 mile

## Slide 12: Kentucky Roadway
AADT = 15,000
Crashes (5 years) = 50
Crash Rate = 179
Length = 1.0 mile
AADT = 30,000
Crashes (5 years) = 85
Crash Rate = 155
Length = 1.0 mile
Casinos save lives!!!

## Slide 13: HSM Implementation

## Slide 14: The HSM is…
Analysis tool
Estimations of safety performance
Prediction of crashes
Notes: The HSM is a toolbox that professionals can use to evaluate or estimate the safety performance of a facility and in this respect is very similar to the Highway Capacity Manual.
The HSM provides users with a process on how to use the tools provided along with direction on which tools are appropriate to use in estimating safety performance.
The HSM provides the user with safety estimates of alternative choices and allows for the development evaluating design options and treatments to improve safety performance.
The HSM provides the required quantitative data for a decision maker to determine the most appropriate solution for a given scenario and support their judgment.

## Slide 15: Kentucky’s HSM Experience
Countermeasure prioritization
Intersection safety evaluation
Before and after analysis

## Slide 16: Work with Kentucky’s HSIP
Focused on 3 countermeasures:
  High Friction Surface Treatment
  Rumble Strips
  Cable Barrier
KYTC wanted to avoid using CRF analysis…
HSM methodologies are being considered for SHIFT

## Slide 17: SPF Development
Average Daily Traffic (ADT)
Crashes/Year
SPF
Notes: Here is an example of how an SPF can be developed.
Assuming that the four data sets depict the crash experience over 5 years for a set of sites with similar features. It can be assumed that the all sites are 2-lane roads with 12-foot lanes, 8-foot shoulders, and no curves.
A curve is fitted through these 4 entities using a negative binomial regression formula. The line is the “best fit” of all the data and is the Safety Performance Function (SPF). The line represents the change in the mean expected number of crashes at all similar entities as ADT (or other exposure measure) increases, while all other factors affecting crash occurrence are held constant. It should be noted that this is an example and typically SPFs are based on a far greater number of sites for greater accuracy.
Sites that lie above the SPF indicate a mean expected crash frequency in excess of the average for comparable sites. One can think about sites with mean risk above the SPF as those with higher than average risk and those below the line as those with lower than average risk.
SPFs have been compiled into safety analysis tools, such as SafetyAnalyst and the Highway Safety Manual (HSM).
However, since crash patterns may vary in different geographical areas, SPFs must be calibrated to reflect local conditions (e.g., driver population, climate, crash reporting thresholds, etc.).

## Slide 18: Regression Model – Safety Performance Function
  where: SPF = predicted number of crashes
  L = section length
  a and b are coefficients that describe the behavior between length, AADT and the estimated number of crashes

## Slide 19
Chart: SPF Comparison
Notes: Kentucky

## Slide 20: Empirical Bayes Estimate
Crashes (corrected for regression to the mean)
EB = (Weight)×SPF+(1-Weight)×Observed Crashes
Notes: Avoid RTM

## Slide 21: Empirical Bayes Weight
where: = predicted number of crashes/year
Y = time frame in years
= overdispersion parameter

## Slide 22: Overdispersion
High phi  SPF good representation on data
Low phi  greater reliance on crash data
SPF
Observed
Crashes
SPF
Observed
Crashes
Notes: Low overdispersion is similar to a lower R2 outliers are not removed: http://www.ncbi.nlm.nih.gov/pubmed/20441841. Phi is proportional to W. If crash data is spread out (like a low R2) then we don’t give as much weight to the model and rely more on site crash data .

## Slide 23
Chart: SPF and Crash Data - Rural Parkway

## Slide 24
Chart: SPF and Crash Data - Rural 4-Lane Divided

## Slide 25: Potential for Crash Reduction
Observed Crashes
EB Crashes (Corrected)
Predicted Crashes from SPF
PCR
Crashes per year
AADT
Notes: Note that all of for specific site

## Slide 26
7 of top 25 PCR are top 25 CRF list
20 of top 25 PCR are in top 100 CRF
Spearman’s Rho of 0.72
SiteID | AADT | Observed | Length | PCR | Crash Rate | CRF
671 | 38672 | 252 | 0.957 | 156.2 | 373.1 | 2.83
512 | 14243 | 178 | 0.513 | 150.8 | 1334.9 | 10.13
29 | 3316 | 90 | 0.389 | 79.1 | 3823.1 | 29.03
472 | 13324 | 105 | 0.643 | 74.6 | 671.6 | 5.10
340 | 10037 | 74 | 0.249 | 63.3 | 1622.4 | 12.32
536 | 15052 | 120 | 1.423 | 49.2 | 307.0 | 2.33
611 | 18691 | 85 | 0.634 | 47.7 | 393.0 | 2.98
253 | 8451 | 50 | 0.125 | 44.7 | 2593.5 | 19.69
375 | 10894 | 61 | 0.533 | 39.4 | 575.6 | 4.37
347 | 10204 | 50 | 0.342 | 36.5 | 785.1 | 5.96
559 | 15742 | 63 | 0.537 | 35.1 | 408.4 | 3.10
652 | 22426 | 40 | 0.088 | 33.7 | 1110.6 | 8.43
631 | 20309 | 135 | 1.674 | 31.9 | 217.6 | 1.65
555 | 15526 | 55 | 0.477 | 30.5 | 406.9 | 3.09
473 | 13518 | 70 | 0.94 | 26.8 | 301.9 | 2.29
669 | 38407 | 68 | 0.427 | 25.9 | 227.2 | 1.72
522 | 14516 | 31 | 0.1 | 25.7 | 1170.2 | 8.88
662 | 25551 | 31 | 0.073 | 25.4 | 910.7 | 6.91
308 | 9364 | 27 | 0.03 | 25.3 | 5266.5 | 39.98
533 | 14833 | 38 | 0.255 | 25.1 | 550.5 | 4.18
647 | 22206 | 82 | 0.869 | 24.8 | 232.8 | 1.77
537 | 15052 | 27 | 0.075 | 22.9 | 1310.5 | 9.95
535 | 14935 | 36 | 0.265 | 22.6 | 498.4 | 3.78
273 | 8887 | 37 | 0.414 | 22.6 | 551.0 | 4.18
SiteID | AADT | Observed | Length | PCR | Crash Rate | CRF
6 | 2605 | 20 | 0.035 | 18.3 | 12019.6 | 91.25
308 | 9364 | 27 | 0.03 | 25.3 | 5266.5 | 39.98
137 | 6268 | 3 | 0.005 | 2.8 | 5245.2 | 39.82
25 | 3234 | 17 | 0.064 | 15.1 | 4500.6 | 34.17
29 | 3316 | 90 | 0.389 | 79.1 | 3823.1 | 29.03
633 | 20581 | 8 | 0.006 | 7.5 | 3549.8 | 26.95
120 | 6088 | 9 | 0.023 | 8.1 | 3521.9 | 26.74
7 | 2605 | 7 | 0.049 | 5.9 | 3004.9 | 22.81
253 | 8451 | 50 | 0.125 | 44.7 | 2593.5 | 19.69
23 | 3183 | 1 | 0.008 | 0.8 | 2151.8 | 16.34
663 | 25551 | 17 | 0.019 | 15.4 | 1918.8 | 14.57
31 | 3492 | 9 | 0.074 | 7.4 | 1908.4 | 14.49
160 | 6814 | 9 | 0.043 | 7.6 | 1683.1 | 12.78
340 | 10037 | 74 | 0.249 | 63.3 | 1622.4 | 12.32
594 | 17790 | 14 | 0.027 | 12.3 | 1597.1 | 12.13
65 | 4608 | 9 | 0.073 | 7.2 | 1466.0 | 11.13
306 | 9299 | 10 | 0.044 | 8.3 | 1339.2 | 10.17
512 | 14243 | 178 | 0.513 | 150.8 | 1334.9 | 10.13
560 | 15742 | 25 | 0.066 | 21.3 | 1318.5 | 10.01
537 | 15052 | 27 | 0.075 | 22.9 | 1310.5 | 9.95
117 | 5920 | 19 | 0.137 | 15.1 | 1283.7 | 9.75
525 | 14602 | 18 | 0.057 | 15.0 | 1185.0 | 9.00
553 | 15456 | 5 | 0.015 | 4.2 | 1181.7 | 8.97
522 | 14516 | 31 | 0.1 | 25.7 | 1170.2 | 8.88
Notes: Rural 4-lane divided SPF Kentucky. Look at site #23: a low AADT and only one crash, yet a CRF of 16. Sites that are not highlighted represent site corrected for RTM or sites where the SPF’s non-linear models better represents the crash data
This shows that they are not drastically different. Different enough to affect the priority of top projects.
Notice the extremely high CRF – site #6. This is likely an intersection. It is a very small section with low AADT and high crashes.

## Slide 27: Comparison of PCRs
PCRs should be compared across similar highway types or functional class
PCRs already account for AADT but much higher PCRs are observed for higher class roadways
This causes higher AADT facilities to rise to the top
Benefit-cost analysis is needed to factor in the cost of an improvement
This becomes unusable for system wide ratings
Notes: You can use different crash types if the countermeasures are different

## Slide 28: Casino Revisited
AADT = 15,000
Crashes (5 years) = 50
Crash Rate = 179
Length = 1.0 mile
AADT = 30,000
Crashes (5 years) = 85
Crash Rate = 155
Length = 1.0 mile
Notes: Based on an actual example in Colorado

## Slide 29
Chart: Rural 4-Lane Divided SPF
y=x^(0.73827)*e^(-3.20716)
phi=0.9345
Notes: SPF scaled for 5 years in unit length (mile).

## Slide 30: Casino Revisited
Before
AADT = 15,000
Crashes (5 years) = 50
Length = 1.0 mile
SPF = 49.0
W = 0.019*
Corrected = 50.0
PCR = 1.0
After
AADT = 30,000
Crashes (5 years) = 85
Length = 1.0 mile
SPF = 81.7
W = 0.011*
Corrected = 85.0
PCR = 3.2
*low model weight
Notes: Idea based on an actual example in Colorado. Note low model weight could be improved with baseline SPF. Not a regression to the mean example but rather CRF assumes crashes are linear compared to AADT

## Slide 31: Before and After
 | AADT | SPF | Observed | Crash Rate | Weight | Corrected | CRF | PCR
Before Casino | 15000 | 49.0 | 50 | 182.6 | 0.019 | 50.0 | 1.077 | 1.0
After Casino | 30000 | 81.7 | 85 | 155.3 | 0.011 | 85.0 | 0.998 | 3.2

## Slide 32: Summary
Casinos aren’t necessarily good for highway safety
Traditional methods have known limitations
  Crashes and AADT aren’t necessarily linearly related
  CRF doesn’t address RTM bias
There are better, more science-based approaches to safety
  The HSM!

## Slide 33: Questions?
Eric Green, PhD, PE, GISP
Kentucky Transportation Center
Research Engineer
eric.green@uky.edu
http://www.ktc.uky.edu
Phone: (859) 257-2680