## Slide 1: Traffic Engineer’s Meeting Tort Liability
Kenneth R. Agent, P.E.
Transportation Research Engineer
Kentucky Transportation Center

## Slide 2
Case Studies
Tort Liability Definitions
Summary of Board of Claims Cases

## Slide 5: Claim
Negligently maintained pedestrian call button
Failed to provide pedestrian sufficient time to cross road with traffic signal
Failed to provide adequate lighting at intersection

## Slide 6: Recommended Order Conclusions of Law
Cabinet exercised engineering judgment in designing phasing at traffic signal (discretionary function)
No MUTCD requirement that Cabinet provide time for pedestrians to cross road (even with no use of pedestrian call button)
Pedestrian crossed road against pedestrian signal

## Slide 7: Conclusions of Law (cont.)
Cabinet had ministerial duty to repair pedestrian button but was not cause of accident since pedestrian did not allow sufficient time for a pedestrian phase to be activated prior to crossing
If Cabinet responsible for intersection lighting, decision is discretionary
Recommends finding in favor of Cabinet

## Slide 8
Notes: Inadequate signing; superelevation; Pic 146, BOC #94-348,439, Amt. Paid $97,500

## Slide 9
Notes: Inadequate signing; superelevation; Pic 146, BOC #94-348,439, Amt. Paid $97,500

## Slide 10
Notes: Inadequate signing; superelevation; Pic 146, BOC #94-348,439, Amt. Paid $97,500

## Slide 11
Notes: Inadequate signing; superelevation; Pic 146, BOC #94-348,439, Amt. Paid $97,500

## Slide 12: Negligence
Failure to use the same standard of care that a reasonably prudent person would

## Slide 13: Standard of Care
Agency directives and policies
Directives of superior agency
Guidelines and policies of similar agencies
Guides developed by national and professional organizations
Textbooks and professional journals
Research results
Expert witnesses

## Slide 14: Comparative Negligence (Depending upon the law)
A Plaintiff who contributed to the plaintiff’s own injury can still collect weighted damages

## Slide 15: Notice (Actual)
Public entity is given specific notice of a defect in the highway system

## Slide 16: Notice (Constructive)
After a reasonable amount of time, the public entity should be aware of a highway defect

## Slide 17: Constructive Notice
Reasonable time between occurrence of defect and when agency becomes aware of defect.
Routine inspection.
Reasonable amount of time?

## Slide 18: Discretionary/Ministerial Acts
Discretionary acts require choice among valid alternatives using judgment
Ministerial acts involve clearly defined tasks not permitting exercise of discretion

## Slide 19: Sovereign Immunity
Began in England where King would not allow suit against himself
No one can sue the government without its permission
Government not responsible for acts of its employees

## Slide 20: Elements Necessary For Negligence
Duty
Breach of Duty
Causal connection between negligent conduct and resulting injury
Actual damages

## Slide 21: Proximate Cause
Cause that leads to the result
Probable consequences of the Negligent Act
Duty and violation of duty
Element of foreseeability
More than one proximate cause

## Slide 22
Notes: Lack warning sign; Pic. 152, BOC # 95-703, Amt. Paid $0

## Slide 23
Notes: Lack warning sign; Pic. 152, BOC # 95-703, Amt. Paid $0

## Slide 24
Notes: Lack warning sign; Pic. 152, BOC # 95-703, Amt. Paid $0

## Slide 25
Notes: Lack warning sign; Pic. 152, BOC # 95-703, Amt. Paid $0

## Slide 26
Notes: Indiana

## Slide 28
Notes: Individual dimissed

## Slide 30: Summary 1981-2009
Number of claims | 15,460
Total amount claimed | $123,068,082
Percent decided | 99
Percent with payment | 49
Total payment | $16,617,604
Percent paid (decided) | 15
Notes: Table 3-1

## Slide 31
Notes: Table 3-1

## Slide 32
Notes: Table 3-1

## Slide 33
*decided claims filed in given year
Notes: Table 3-2

## Slide 34
Notes: Table 3-7

## Slide 35: Reasons for Highest Number of Claims
Notes: Table 3-9

## Slide 36
Reasons for Highest Amounts of Claims

## Slide 37: Amount Claimed $50,000 and above $millions
Notes: Table 4-1

## Slide 38: Claim Amount Paid of $50,000 or More
Notes: Table 4-1

## Slide 39: Districts with Most Claims by Reason $50,000 and Above
Reason | District
Traffic Control Devices | 7
Drainage | 12
Barrier | 2
Road Surface Related | 12
Shoulder Related | 7
Construction Zone-Traffic Control | 6
Geometric Feature | 1
State Vehicle Operation | 2
Maintenance Activity | 12
Construction Activity | 5
Fixed Object | 11
Notes: Table 4-2

## Slide 40
Notes: Signing on stop approach; Pic 105; BOC #90-581, Amt. Paid $15,000

## Slide 41
Notes: Signing on stop approach; Pic 105; BOC #90-581, Amt. Paid $15,000

## Slide 42
Notes: Signing on stop approach; Pic 105; BOC #90-581, Amt. Paid $15,000

## Slide 43
Notes: Sight distance at intersection; Pic 211, BOC #99-969, Amt. Paid $12,500

## Slide 44
Notes: Sight distance at intersection; Pic 211, BOC #99-969, Amt. Paid $12,500

## Slide 45
Notes: Sight distance at intersection; Pic 211, BOC #99-969, Amt. Paid $12,500

## Slide 46
Notes: Sight distance at intersection; Pic 211, BOC #99-969, Amt. Paid $12,500

## Slide 47
Notes: Traffic control at intersection; Pic 39, BOC #88-1120, Amt. Paid $73,394

## Slide 48
Notes: Traffic control at intersection; Pic 39, BOC #88-1120, Amt. Paid $73,394

## Slide 49
Notes: Traffic control at intersection; Pic 39, BOC #88-1120, Amt. Paid $73,394

## Slide 50
Notes: Traffic control at intersection; Pic 39, BOC #88-1120, Amt. Paid $73,394

## Slide 51
Notes: Improper warning signs for curve; Pic 171, BOC #92-531, Amt. Paid $0

## Slide 52
Notes: Improper warning signs for curve; Pic 171, BOC #92-531, Amt. Paid $0

## Slide 53
Notes: Car ran off road into creek (no GR or signs); Pic 277, BOC #08-1195/1199

## Slide 54
Notes: Car ran off road into creek (no GR or signs); Pic 277, BOC #08-1195/1199

## Slide 55
Notes: Car ran off road into creek (no GR or signs); Pic 277, BOC #08-1195/1199

## Slide 56
Notes: No warning sign; no signs (police photos); Pic 156, BOC #94-594, Amt. Paid $0

## Slide 57
Notes: No warning sign; no signs (police photos); Pic 156, BOC #94-594, Amt. Paid $0

## Slide 58
Notes: Object marker; Pic 131, BOC #93-637, Amt. Paid $$25,000

## Slide 59
Notes: Object marker; Pic 131, BOC #93-637, Amt. Paid $$25,000

## Slide 60
Notes: Object marker; Pic 131, BOC #93-637, Amt. Paid $$25,000

## Slide 61
Notes: Lack of signing; Pic 258; BOC #05-786

## Slide 62
Notes: Lack of signing; Pic 258; BOC #05-786

## Slide 63
Notes: Lack of signing; Pic 258; BOC #05-786

## Slide 64
Notes: Sign (deer); Pic 142, BOC #93-479, Amt. Paid $0

## Slide 65
Notes: Sign (deer); Pic 142, BOC #93-479, Amt. Paid $0

## Slide 66
Notes: Sign placement; Pic 229, BOC #02-373; Amt. Paid $0

## Slide 67
Notes: Sign placement; Pic 229, BOC #02-373; Amt. Paid $0

## Slide 68
Kenneth R. Agent, P.E.
Transportation Research Engineer
Kentucky Transportation Center
University of Kentucky
176 Raymond Building
Lexington, KY 40506
(859) 257-4507
ken.agent@uky.edu