## Slide 1
CULVERT PIPE REPLACEMENT DETAIL – Mill & Inlay w pipes
1’-0”
1’-0”
Pipe Dia.
3”
1’-0”
Min.
10” Asphalt Base
Flowable Fill
(Incidental to Culvert Pipe)
Culvert Pipe Replacements – Initial Backfill
Culvert Pipe Replacements shall be constructed according to the Initial Backfill detail shown above, or as directed by the Engineer. Allow the asphalt base to be exposed to traffic a minimum of 14 days to allow for settlement. After the 14-day waiting period, mill and inlay 1.25 inches of asphalt surface according to the detail below.
Existing Pavement
50 FT
50 FT
Asphalt Base
Flowable Fill
Milling and Texturing Asphalt Surface
1.25” Asphalt Surface
Delete information in yellow and verify information in blue

## Slide 2
CULVERT REPLACEMENT DETAIL – Mill & Inlay w pipes and RCBCs
Culvert Pipe or Box Culvert Replacements shall be constructed according to the Initial Backfill detail shown above, or as directed by the Engineer. Allow the asphalt base to be exposed to traffic a minimum of 14 days to allow for settlement. After the 14-day waiting period, mill and inlay 1.25 inches of asphalt surface according to the detail below.
Culvert Pipe or Box Culvert Replacements – Initial Backfill
1’-0”
1’-0”
Pipe Dia. or
RCBC Width
3”
1’-0”
Min.
10” Asphalt Base
Flowable Fill
(Incidental to Culvert Pipe)
Existing Pavement
50 FT
50 FT
Asphalt Base
Flowable Fill
Milling and Texturing Asphalt Surface
1.25” Asphalt Surface
Culvert Replacement – All Locations Except STA 382+74 EB lane
Delete information in yellow and verify information in blue

## Slide 3
CULVERT PIPE REPLACEMENT DETAIL – Pipes - Resurfacing and no mill
1’-0”
1’-0”
Pipe Dia.
3”
1’-0”
Min.
10” Asphalt Base
Flowable Fill
(Incidental to Culvert Pipe)
Culvert Pipe Replacements – Initial Backfill
Culvert Pipe Replacements shall be constructed according to the Initial Backfill detail shown above, or as directed by the Engineer. Allow the asphalt base to be exposed to traffic a minimum of 14 days to allow for settlement before placing the asphalt surface.
Existing Pavement
Asphalt Base
Flowable Fill
1.25” Asphalt Surface
Delete information in yellow and verify information in blue

## Slide 4
CULVERT REPLACEMENT DETAIL – Pipes and RCBCs w resurfacing and no mill
Culvert Pipe or Box Culvert Replacements shall be constructed according to the Initial Backfill detail shown above, or as directed by the Engineer. Allow the asphalt base to be exposed to traffic a minimum of 14 days to allow for settlement before placing the asphalt surface.
Asphalt Base
Flowable Fill
1.25” Asphalt Surface
Culvert Pipe or Box Culvert Replacements – Initial Backfill
1’-0”
1’-0”
Pipe Dia. or
RCBC Width
3”
1’-0”
Min.
10” Asphalt Base
Flowable Fill
(Incidental to Culvert Pipe)
Existing Pavement
Delete information in yellow and verify information in blue