SPECIAL NOTE FOR PORTABLE CHANGEABLE MESSAGE SIGNS

This Special Note will apply when indicated on the plans or in the proposal.

1.0	DESCRIPTION.  Furnish, install, operate, and maintain variable message signs at the locations shown on the plans or designated by the Engineer.  Remove and retain possession of variable message signs when they are no longer needed on the project.

2.0	MATERIALS.

2.1	General.  Use LED Variable Message Signs Class I, II, or III, as appropriate, from the Department’s List of Approved Materials.

Unclassified signs may be submitted for approval by the Engineer. The Engineer may require a daytime and nighttime demonstration.  The Engineer will make a final decision within 30 days after all required information is received.

2.2	Sign and Controls.  All signs must:

- Provide 3-line messages with each line being 8 characters long and at least 18 inches tall.  Each character comprises 35 pixels.

- Provide at least 40 preprogrammed messages available for use at any time.  Provide for quick and easy change of the displayed message; editing of the message; and additions of new messages.

- Provide a controller consisting of:

- Keyboard or keypad.

- Readout that mimics the actual sign display.  (When LCD or LCD type readout is used, include backlighting and heating or otherwise arrange for viewing in cold temperatures.)

- Non-volatile memory or suitable memory with battery backup for storing pre-programmed messages.

- Logic circuitry to control the sequence of messages and flash rate.

4)	Provide a serial interface that is capable of supporting complete remote control ability through land line and cellular telephone operation.  Include communication software capable of immediately updating the message, providing complete sign status, and allowing message library queries and updates.

- Allow a single person easily to raise the sign to a satisfactory height above the pavement during use, and lower the sign during travel.

- Be Highway Orange on all exterior surfaces of the trailer, supports, and controller cabinet.

- Provide operation in ambient temperatures from -30 to + 120 degrees Fahrenheit during snow, rain and other inclement weather.

- Provide the driver board as part of a module.  All modules are interchangeable, and have plug and socket arrangements for disconnection and reconnection.  Printed circuit boards associated with driver boards have a conformable coating to protect against moisture.

- Provide a sign case sealed against rain, snow, dust, insects, etc.  The lens is UV stabilized clear plastic (polycarbonate, acrylic, or other approved material) angled to prevent glare.

- Provide a flat black UV protected coating on the sign hardware, character PCB, and appropriate lens areas.

- Provide a photocell control to provide automatic dimming.

- Allow an on-off flashing sequence at an adjustable rate.

- Provide a sight to aim the message.

- Provide a LED display color of approximately 590 nm amber.

- Provide a controller that is password protected.

- Provide a security device that prevents unauthorized individuals from accessing the controller.

- Provide the following 3-line messages preprogrammed and available for use when the sign unit begins operation:

/KEEP/RIGHT/(((/

/KEEP/LEFT/(((/

/LOOSE/GRAVEL/AHEAD/

/RD WORK/NEXT/**MILES/

/TWO WAY/TRAFFIC/AHEAD/

/PAINT/CREW/AHEAD/

/REDUCE/SPEED/**MPH/

/BRIDGE/WORK/***0 FT/

/MAX/SPEED/**MPH/

/SURVEY/PARTY/AHEAD/

/MIN/SPEED/**MPH/

/ICY/BRIDGE/AHEAD/  /ONE

LANE/BRIDGE/AHEAD/

/ROUGH/ROAD/AHEAD/

/MERGING/TRAFFIC/AHEAD/

/NEXT/***/MILES/

/HEAVY/TRAFFIC/AHEAD/

/SPEED/LIMIT/**MPH/

/BUMP/AHEAD/

/TWO/WAY/TRAFFIC/

*Insert numerals as directed by the Engineer.

Add other messages during the project when required by the Engineer.

2.3	Power.

- Design solar panels to yield 10 percent or greater additional charge than sign consumption.  Provide direct wiring for operation of the sign or arrow board from an external power source to provide energy backup for 21 days without sunlight and an on-board system charger with the ability to recharge completely discharged batteries in 24 hours.

3.0	CONSTRUCTION.  Furnish and operate the variable message signs as designated on the plans or by the Engineer.  Ensure the bottom of the message panel is a minimum of 7 feet above the roadway in urban areas and 5 feet above in rural areas when operating.  Use Class I, II, or III signs on roads with a speed limit less than 55 mph.  Use Class I or II signs on roads with speed limits 55 mph or greater.

Maintain the sign in proper working order, including repair of any damage done by others, until completion of the project.  When the sign becomes inoperative, immediately repair or replace the sign.  Repetitive problems with the same unit will be cause for rejection and replacement.

Use only project related messages and messages directed by the Engineer, unnecessary messages lessen the impact of the sign.  Ensure the message is displayed in either one or 2 phases with each phase having no more than 3 lines of text.  When no message is needed, but it is necessary to know if the sign is operable, flash only a pixel.

When the sign is not needed, move it outside the clear zone or where the Engineer directs.  Variable Message Signs are the property of the Contractor and shall be removed from the project when no longer needed.  The Department will not assume ownership of these signs.

4.0	MEASUREMENT.  The final quantity of Variable Message Sign will be the actual number of individual signs acceptably furnished and operated during the project. The Department will not measure signs replaced due to damage or rejection.

5.0	PAYMENT.  The Department will pay for the Variable Message Signs at the unit price each.  The Department will not pay for signs replaced due to damage or rejection.  Payment is full compensation for furnishing all materials, labor, equipment, and service necessary to, operate, move, repair, and maintain or replace the variable message signs. The Department will make payment for the completed and accepted quantities under the following:

Code	Pay Item								Pay Unit

02671	Portable Changeable Message Sign		Each

Effective June 15, 2012