## Slide 1
SPR 23-636
Accommodating Innovative Uses of Public Right of Way
KENTUCKY TRANSPORTATION CENTER
David Moses, PE, PLS
Research Engineer
Kentucky Transportation Center
david.moses@uky.edu
Jennifer McCleve, PE
Utilities and Rail Branch Manager
Kentucky Transportation Cabinet
jennifer.mccleve@ky.gov

## Slide 2
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER
Renewable/Alternative Power
  Solar
  Wind
Broadband
Small Cell Wireless
Connected Autonomous Vehicle Equipment
Electric Vehicle Charging Stations
Clean Energy and Connectivity (CEC) Uses

## Slide 3
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER
CEC Uses Along Highway
Facilities Owned By Others and Subject to KYTC Utility Accommodation Policy
Proposed KYTC Projects - Utilities Function within the Division of Right of Way and Utilities
Existing KYTC Roadways – Permits Function within the Division of Maintenance
Study Focus

## Slide 4
Clean Energy and Connectivity (CEC) Uses

## Slide 5
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER
States are using Solar and Wind Power to:
Power State Buildings (Maintenance Garage, Rest Areas, Welcome Centers)
Street/Parking Lot Lighting
Crosswalk Visibility
Weigh in Motion Systems
EV Charging
Road and Bridge Lighting
Radar Sensors
Roadway Signs
Pavement Markers

## Slide 6
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER
KENTUCKY TRANSPORTATION CENTER
  Within highway right of way
    Interchange, roadway & bridge lighting
    Signage
    Rest areas
  Roof mounted on building facilities
  Canopies for parking areas and parking garages
  Electric vehicle charging stations
  Small equipment
    Signs
    Sensors
    Markers
https://electrek.co/2022/09/13/modular-solar-ev-charger/
Specific Examples of DOT Uses of Solar

## Slide 7
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER
Three types of scaled systems
  Residential
    Roof mounted
    Offset home energy use
  Commercial and industrial
    Similar but larger scale than residential systems
    Roof mounted, parking lot canopies, open fields
    Offset energy use and can be a revenue source
  Utility
    Very large scale
    Sell electricity to utility companies or owned by them
Types of Solar Installations

## Slide 8
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER
KENTUCKY TRANSPORTATION CENTER
Three solutions
  Grid-tied
    Connected to existing power grid
    Power supplied by grid during low energy production periods
  Off-grid
    Not connected to existing power grid
    Reliability on solar production only
    Battery system for storage for use during low energy production periods
  Hybrid
    Connected to existing power grid
    Use battery system for storage
    Most flexible – power can be provided by grid or battery during low energy production periods
Types of Solar Installations

## Slide 9
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER
KENTUCKY TRANSPORTATION CENTER
Equipment required
  Solar photovoltaic (PV) panels
    Convert solar energy to electricity
  Inverter
    Convert direct current (DC) electricity into alternating current (AC) electricity
  Racking and mounting systems
    Fixed or sun tracking
  Monitoring system
  Energy storage
    Battery or grid tie
  Charge controller
    Regulates charging to battery
Types of Solar Installations

## Slide 10
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER
KENTUCKY TRANSPORTATION CENTER
  One wind turbine can generate the same amount of electricity as ~48,704 solar panels
  Most facilities located in rural areas
    Require a lot of land
    Many consider turbines an eyesore and source of noise pollution
    Can be dangerous to wildlife
    Wind speeds can vary hour to hour and season to season affecting output
    Three solutions
      Utility-scale – 100kW to several MW to grid
      Offshore – typically largest turbines and utility-scale generally
      Distributed – less than 100kW
        Supplement a home, farm, or business on grid
        Provide power off grid
Wind Power

## Slide 11
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER
Equipment required
  Tower
    Supports turbine at heights up to 300 feet
  Nacelle
    Housing that contains components that convert wind energy to electricity
  Hub
    Attaches blades to nacelle and facilitates rotation
  Blades
    Typically three in an airfoil shape (horizontal)
  Inverter
    Converts DC electricity to AC
  Storage
    Battery or grid connection for net metering
Wind Power

## Slide 12
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER

## Slide 13
KENTUCKY TRANSPORTATION CENTER
US Wind Turbine Database

## Slide 14
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER
    Always-on high-speed internet access data transmitted through:
      Digital subscriber line (DSL) – telephone lines
      Cable – coaxial cable (television)
      Fiber optic – pulses of light through flexible glass or tubing
      Wireless – radio frequencies between a local receiver and a tower or other fixed device
      Satellite – between an orbiting satellite and receiver
      Mobile – mobile device such as a smartphone
        Accommodation within right of way
          Telephone, cable, and fiber optic – currently
          Mobile – developing technology to be expanded upon with discussion of small cell wireless and C/AV
Broadband

## Slide 15
KENTUCKY TRANSPORTATION CENTER

## Slide 16
KENTUCKY TRANSPORTATION CENTER
Kentucky Broadband Efforts
Kentucky Wired
  State-run project constructing over 3,000 miles of “middle mile” high-speed, high-capacity fiber optic cable
  Connecting government offices, universities, community colleges, state police posts, state parks, and other government institutions
Kentucky Office of Broadband Development
  Manage various state and federal funds for “last mile” broadband infrastructure projects
  Private companies eligible for grants

## Slide 17
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER

## Slide 18
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER
      Small radio antennas that provide short-range wireless data transmission within small areas
      Small cell facilities densify coverage when macrocell towers reach capacity
      Requires little power
      Equipment
        Radio equipment and antenna
        Require power, backhaul, and a permitted space
        Can be constructed on streetlights, utility poles, sides of buildings, etc
What is Small Cell Wireless

## Slide 19
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER
What is Small Cell Wireless
      Mobile broadband and significant contributor to enabling 5G
      Accommodates significantly higher data transfer rates than previous technology
      Small Cell Range ~ 1.5 miles
      Macrocell towers – what we are familiar with (range ~ 25 miles)
      Typically connected directly to fiber (backhaul)
        Microwave transmission back to macrocell could be used for backhaul (rural areas)
        Owners tend to be the three major wireless providers
        SHE Memo dated June 18, 2017

## Slide 20
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER
KENTUCKY TRANSPORTATION CENTER
      Connected vehicles – communicate with other vehicles or infrastructure
      Autonomous vehicles – can operate without a human driver
      For study focus on connected vehicles as autonomy results from connection
      Vehicles are already equipped with some level of connection (Adaptive Cruise Control, Real Time Route Planning)
      Connected vehicles communicate with other vehicles and infrastructure
        GPS
        Broadband wireless
        Cellular networks
        Future technology will need to accommodate thousands of connections simultaneously
V2I – Vehicle to infrastructure
V2N – Vehicle to network
V2V – Vehicle to vehicle
V2P – Vehicle to pedestrian
V2X – Vehicle to everything
Connected and Autonomous Vehicles
C/AV Network Architecture

## Slide 21
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER
KENTUCKY TRANSPORTATION CENTER
      Equipment
        OBUs – on board units
        RSUs – roadside units
        For this study, focus on roadside units
          Similar in size to small cell units
          Can be connected to infrastructure – signs, poles, etc.
          Continuously evolving
            USDOT has published report for standardizing roadside units
Connected and Automated
Vehicles

## Slide 22
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER
KENTUCKY TRANSPORTATION CENTER
        Managed by Division of Planning
        Goals and objectives
          Evaluate Feasibility of dedicated C/AV lanes or other configurations on I-64 between Louisville and Lexington
          Suitability of the corridor to C/AV operations
          Upgrades needed to implement those operations
KYTC Item No. 5-577
            Scope Items
            Identify legal and regulatory hurdles and potential enabling legislation
            Assess potential impacts to traffic
            Identify and plan improvements to the corridor
            Provide cost estimates and identify potential funding strategies
            Intentionally engage stakeholders
            Scope of work
            Analyze infrastructure needs
              System: digital and operational (hardware/software/edge computing)
              Roadway: widening/striping/signage
              Utilities: communication/broadband/power/ conduit
              Identify and consider maintenance operations

## Slide 23
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER
KENTUCKY TRANSPORTATION CENTER
EV Charging Stations
KY's Electric Vehicle Charging Program is well underway
Round 1 RFP Proposal due date: August 24, 2023
Selected Developers will be responsible for: site acquisition, design, purchase, construction, installation of hardware and software, operation and maintenance (O&M), and reporting services for a given Project
KYTC will not own the sites
Sites cannot be on KYTC right of way
Follow this effort and learn from their experiences

## Slide 24
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER
KENTUCKY TRANSPORTATION CENTER
EV RFP
Corridor
Group
Map

## Slide 25
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER
KENTUCKY TRANSPORTATION CENTER
EV
Stakeholder Engagement

## Slide 26
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER
KENTUCKY TRANSPORTATION CENTER
Kentucky EV Website
https://kyevcharging.com
Contact Information
EVChargingProgram@ky.gov

## Slide 27: Current Regulatory Framework and Challenges
KENTUCKY TRANSPORTATION CENTER
Federal Accommodation Options
State Definition of Utilities
Mobile Now Act
Ownership and Agreements
Regulatory Challenges
Private Involvement

## Slide 28
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER
KENTUCKY TRANSPORTATION CENTER
Two Methods To Accommodate CEC Uses Under Federal Regulation
Utility – 23 CFR part 645
State DOT Utility Accommodation Policy governs
FHWA approved UAP programmatically
Approvals required for changes in access on federal aid highways
Fees charged at the state’s discretion
Safety and operation cannot be impacted
Alternative Use of Right-of-Way – 23 CFR part 710
FHWA requires a public interest finding
Required for each individual use
Approvals required for changes in access on federal aid highways
Fair market rent usually required, FHWA has determined CEC excepted
Safety and operations cannot be Impacted

## Slide 29
Definition of a Utility under KRS 278.010
Any natural persons, partnerships, corporations, and two (2) or more persons having a joint or common interest…who owns, controls, operates, or manages any facility used or to be used for or in connection with:
(a) The generation, production, transmission, or distribution of electricity to or for the public, for compensation, for lights, heat, power, or other uses
(b) The production, manufacture, storage, distribution, sale, or furnishing of natural or manufactured gas, or a mixture of same, to or for the public, for compensation, for light, heat, power, or other uses
(c) The transporting or conveying of gas, crude oil, or other fluid substance by pipeline to or for the public, for compensation
(d) The diverting, developing, pumping, impounding, distributing, or furnishing of water to or for the public, for compensation
(e) The transmission or conveyance over wire, in air, or otherwise, of any message by telephone or telegraph for the public, for compensation
(f) The collection, transmission, or treatment of sewage for the public, for compensation, if the facility is a subdivision collection, transmission, or treatment facility plant that is affixed to real property and is located in a county containing a city of the first class or is a sewage collection, transmission, or treatment facility that is affixed to real property, that is located in any other county, and that is not subject to regulation by a metropolitan sewer district or any sanitation district created pursuant to KRS Chapter 220

## Slide 30: Mobile Now Act
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER
Signed into law on March 23, 2018
Prescribes additional requirements to facilitate the installation of broadband
State DOT must:
  Identify a broadband utility coordinator
  Include broadband in the utility process
Not a mandate to allow broadband in right of way

## Slide 31
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER
Benefits
  KYTC does not have the expertise to operate and maintain most of the equipment and systems required for these uses
  Upfront costs can be mitigated by having private companies handle the construction
Drawbacks
  May have conflicting interests with KYTC in terms of how they treat our right-of-way
  Private Involvement

## Slide 32
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER
Self Ownership
Public-Private Partnership (P3):
  Third Party PPA
  Solar Lease/License Revenue
  Morris Model
Traditional Power Purchase Agreement (PPA)
Ownership and Development Models for
Renewable Energy Projects
Notes: Third Party PPA - private entity to design, build, finance, operate, and maintain (or any combination thereof) a solar project, with little to no upfront capital investment required by KYTC
Solar Lease / License Revenue (P3). KYTC would lease unused land within the right of-way to a private developer, who would develop a solar project and make set land lease payments to KYTC
Morris Model (P3) hybrid PPA and bond issuance model, a private developer would design, build, operate, and maintain (or any combination thereof) a project, with Caltrans and the Department of Treasury providing
low-rate financing.
Utility Contract - KYTC would have a standard PPA contract with a local utility with set rates and terms

## Slide 33
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER
  23 USC 11
    Prohibits commercial activity within the Interstate ROW from serving motor vehicle users
    Limits commercial activities in rest areas for serving motor vehicle users. Limited activities that are allowed in rest areas include:
      Certain advertising and displays related to tourism, historical events, travel related information
      Vending machines with preferences given to vendors operating under the Randolph-Sheppard Act
      Any revenue must be used to maintain rest areas
  Legality of PPA’s in Kentucky
  Regulatory Challenges

## Slide 34
RESEARCH
ABSTRACT
DESIGN
KENTUCKY TRANSPORTATION CENTER
Study Tasks
Task | Description | Status
1 | Review literature and transportation agency guidance on innovative uses of public ROW. | 
2 | Identify issues with current regulatory framework and recommend changes to legislation that would be necessary. | 
3 | Assess requirements for CEC applications on public ROW (e.g., electrical, land area, topography, special hardware, roadway modifications, clear zones). | 
4 | Establish material and locational standards for developing CEC facilities. Evaluate costs associated with each facility type. | 
5 | Identify general areas and/or corridors within the public ROW suitable for each CEC application. | 
6 | Prepare a technical brief and implementation plan, which describes how KYTC can accommodate innovative uses of its ROW | 

## Slide 35
RESEARCH
KENTUCKY TRANSPORTATION CENTER
KENTUCKY TRANSPORTATION CENTER
Possible Opportunities
Rest Areas – Renewables
Interchanges - Renewables
Park & Rides – Renewables, Charging Stations
Abandoned Utility Corridors - Broadband
Excess Right of Way – Broadband, Renewables
Existing Lighting Infrastructure and Utility Poles – Small Cell Wireless & CAV

## Slide 36
RESEARCH
KENTUCKY TRANSPORTATION CENTER
KENTUCKY TRANSPORTATION CENTER
Thank You !
David Moses, PE, PLS
Research Engineer
Kentucky Transportation Center
david.moses@uky.edu
Jennifer McCleve, PE
Utilities and Rail Branch Manager
Kentucky Transportation Cabinet
jennifer.mccleve@ky.gov