## Slide 1: Design Speed
Bill Gulick PE PLS

## Slide 2: Speed, Speed, Speed, Speed
Running Speed
  Length / Time (used in cost analysis etc.)
Operating Speed
  Observed Speed (speed studies 85th percentile)
Posted Speed
  White Sign (speed limit)
Design Speed
  A selected speed used to determine the geometric features of the highway. (AASHTO 2011)

## Slide 3: Design Speed
First Defined in 1936 (by Barnett)
AASHO accepted 1938
  “The maximum uniform speed which probably will be adopted by the faster group of drivers but not, by the small percentage of reckless ones.”
Definition Changed over Time
  1936, 1938, 1940, 1941, 1945, 1954, 1973, 1977, 1984, 1988, 1994, 1997, 2004, 2011
AASHTO 1973 (1973 – 1994 + sort of)
  “The maximum safe speed that can be maintained over a specified section of highway when conditions are so favorable that the design features of the highway govern.”

## Slide 4: Design Speed
Current definition is the 14th (I think)
  AASHTO Green Book 2011 “A selected speed used to determine the various geometric design features of the highway.”
14 Words to define and 19 paragraphs advising how to pick a good (appropriate) one.
  Logical
  All feature related to obtain balance
  Above minimum where feasible
  Meet Driver Expectation (where practical)
  Within constraints of S.E.E. (social, environmental, economics)

## Slide 5: Design Speed
More Advice on Design Speed
  On low speed facilities above minimum criteria may encourage higher speeds.
  Higher Design Speeds are Appropriate for Higher Functional Class Roadways
  Design Speed is not particularly relevant in (true < 45mph)Urban Areas. (except for sight distances).
  Critical element in Rural Areas is Horizontal Curves and Superelevation.
  Design Speed should reflect the desired Operating Speed

## Slide 6: Design Speed
Other Factors (more advice)
  Posted Speed (PS) good correlation with Operating Speed (OS)
  Design Speed (DS) little correlation with OS
  DS < PS = Lower Speeds (minor correlation)
  DS > PS = Higher Speeds (more correlation)
  Bigger Right Shoulder = Higher Speeds
  Bigger Median = Higher Speeds
  Note lack of the word “safe” in new definition.
  Liability Associated with DS vs. PS over stated.

## Slide 7: Design Speed
KYTC Highway Design Manual (2008 edition)
  Design Speed is a selected speed used to determine the various geometric features of the roadway. It is the highest continuous speed at which individual vehicles can travel with safety upon a highway when weather conditions are favorable, traffic density is low, and the geometric design features of the highway are the governing conditions for safe speed.
  1970’s again in mid 90’s (not mid 80’s)…. Until 1994

## Slide 8: Design Speed
DESIGN SPEED Per revised NEW DESIGN MANUAL: KYTC HD-703
  Design speed is a selected speed used to determine the various geometric features of the roadway.
The selected design speed should be a logical one with respect to the anticipated operating speed, topography, the adjacent land use, and the functional classification of the highway. In selecting the design speed, every effort should be made to attain a desired combination of safety, mobility, and efficiency within the constraints of environmental impacts, economics, project scope, aesthetics, and social or political impacts.
The selected design speed should be consistent with the speed that drivers are likely to expect on a given highway facility. For a further discussion of the philosophy of design speed, see AASHTO's “A Policy on Geometric Design of Highways and Streets”.

## Slide 9: Design Speed
2011 AASHTO Green Book Minimum Recommended Design Speeds
Local Roadways:
  Rural Local: Chapter 5, Section 5.2.1, Table 5-1 (Minimum Design Speed for Local Rural Roads).
  Urban Local: Chapter 5, Section 5.3.1
Collector Roadways:
  Rural Collector: Chapter 6, Section 6.2.1, Table 6-1 (Minimum Design Speed for Rural Collectors).
  Urban Collector: Chapter 6, Section 6.3.1
Arterial Roadways:
  Rural Arterial: Chapter 7, Section 7.2.2
  Urban Arterial: Chapter 7, Section 7.3.2

## Slide 10: Design Speed
2005 AASHTO Design Standards Interstate System
Interstates
  Rural: Page 2
  Urban: Page 2
2016 KYTC Highway Design Manual
Chapter 700 Geometric Design Guidelines:
  Exhibit 700-01 COMMON GEOMETRIC PRACTICES RURAL LOCAL ROADS
  Exhibit 700-02 COMMON GEOMETRIC PRACTICES RURAL COLLECTOR ROADS
  Exhibit 700-03 COMMON GEOMETRIC PRACTICES RURAL ARTERIAL ROADS
  Exhibit 700-04 COMMON GEOMETRIC PRACTICES URBAN ROADWAYS

## Slide 11: Design Speed
FHWA OLD 13 Controlling Criteria (1985)
Design Speed
Lane Width
Shoulder Width
Bridge Width
Structure Capacity
Horizontal Alignment
Vertical Alignment
Grade
Stopping Sight Distance
Cross-Slope
Superelevaion
Vertical Clearance
Horizontal Clearance/Lateral Offset
FHWA NEW 10–2 (KYTC) Controlling Criteria (2016)
Design Speed
Lane Width
Shoulder Width
Horizontal Curve
Superelevation Rate
Stopping Sight Distance (SDD)
Maximum Grade
Cross-Slope
Vertical Clearance
Design Load (Structure Capacity)
Under 50 mph
Design Speed
Design Load (Structure Capacity)

## Slide 12: Design Speed
THANK
YOU
ANY QUESTIONS??

## Slide 13: DOT
AASHTO Green Book
AASHTO Roadside Design Guide

## Slide 14: Design Speed
2016 Highway Design Manual:
Design speed is a selected speed used to determine the various geometric features of the roadway.
  The selected design speed should be a logical one with respect to the anticipated operating speed, topography, the adjacent land use, and the functional classification of the highway. In selecting the design speed, every effort should be made to attain a desired combination of safety, mobility, and efficiency within the constraints of environmental impacts, economics, project scope, aesthetics, and social or political impacts.