## Slide 1: HSM, SHIFT, and Data Access Tool

## Slide 2: Agenda
Highway Safety Manual
SHIFT integration
Crash Data Access Tool (CDAT)
  HIVEi vs CDAT
  New crash analysis
  Demo
  Discovering crash errors
  Future of CDAT

## Slide 3: Why the Highway Safety Manual

## Slide 4
Improving Formula Components

## Slide 5: HIVEi verses CDAT

## Slide 7: Comparison
HIVEi
Uses TED
  Crash and roadway data updated frequently throughout the year
  Useful for analysis in-between calendar year (year-to-date)
  Useful for current roadway conditions
CDAT
Uses… BILL
  Crash and roadway data updated annually
    April
  Static data used for annual comparisons (apples and apples)
  Crash data is post-processed
  Crashes are linked to historical road conditions

## Slide 8: A New Approach to Highway Safety
HSM

## Slide 9: Critical Rate Analysis
The old way of quantifying safety

## Slide 10: Critical Rate Analysis
Traditional way to quantify safety
Comparison of a section of road to an average section of road of a similar type
Comparison of the average rate to that of the critical rate (incorporates a 99.5% confidence)

## Slide 11: Critical Numbers
Critical numbers were calculated
Nc = critical number of crashes
Na = average number of crashes
K = constant related to level of statistical significance selected (a probability of 0.995 was used, K = 2.576)

## Slide 12: Using the Buildup – Critical #
Consult Table 6 for the Critical Number to Use Based on the Roadway Type

## Slide 13: Critical Crash Rates
Cc = critical crash rate
Ca = average statewide crash rate for type of intersection
K = constant related to level of statistical significance selected (a probability of 0.995 was used, K = 2.576)
M = exposure (M is in terms of million vehicles (MV)

## Slide 14: Actual Crash Rates
Section (C/100 MVM):
N = Number of Crashes
Y = Number of Years
AADT= Average Annual Daily Traffic
L = Length (miles)
Spot (C/MV):

## Slide 15: Critical Rate Factor
Ratio of Actual Rate over Critical Rate
CRFs over 1 are more “dangerous” than the average section
Typically sorted descending
Prioritization lists can be generated from the top X percentage

## Slide 16: Regression to the Mean
Chart: Year
Series 1 | 5 | 3 | 2 | 4 | 5 | 3 | 6 | 4 | 3 | 5 | 6 | 7 | 4 | 3 | 5 | 2 | 4 | 6
Notes: Crash frequencies vary naturally from one time period to the next and therefore, a site that has an above-average crash frequency one year is likely to have a below-average crash frequency the next. Statistical methods can be used to assure that these changes are not mistaken as the effects of roadway enhancement project.

## Slide 17: Regression to the Mean
AFTER
BEFORE
Site Selected
for Treatment
due to Short-Term Trend
Perceived Effectiveness of Treatment
Expected Average
Crash Frequency
(Without Treatment)
RTM Reduction
Actual Reduction due to Treatment
Observed Crashes
Notes: The steps used to apply the EB Method are as follows:
Determine if the EB Method is applicable;
Determine if crash data is available for the time period used for prediction;
Apply the EB Method to estimate the expected crash frequencies by combining the predicted and observed values; and
Adjust the estimated value of expected crashes to a future time period, if appropriate.
A.2.1 Determine whether the EB method is applicable
The applicability of the EB Method to a particular project or facility depends on the type of analysis being performed and the type of future project work that is anticipated. If the analysis is being performed to assess the expected average crash frequency of a specific highway facility, but is not part of the analysis of a planned future project, then the EB Method should be applied. If a future project is being planned, then the nature of that future project should be considered in deciding whether to apply the EB Method.
The EB Method should be applied for the analyses involving the following future project types:
Sites at which the roadway geometrics and traffic control are not being changed (e.g., the “do-nothing” alternative),
Projects in which the roadway cross section is modified but the basic number of through lanes remains the same (This would include, for example, projects for which lanes or shoulders were widened or the roadside was improved, but the roadway remained a rural two-lane highway);
Projects in which minor changes in alignment are made, such as flattening individual horizontal curves while leaving most of the alignment intact;
Projects in which a passing lane or a short four-lane section is added to a rural two-lane, two-way road to increase passing opportunities; and
Any combination of the above improvements.
The EB Method is not applicable to the following types of improvements:
Projects in which a new alignment is developed for a substantial proportion of the project length; and
Intersections at which the basic number of intersection legs or type of traffic control is changed as part of a project.
The reason that the EB Method is not used for these project types is that the observed crash data for a previous time period is not necessarily indicative of the crash experience that is likely to occur in the future after such a major geometric improvement. Since, for these project types, the observed crash frequency for the existing design is not relevant to estimation of the future crash frequencies for the site, the EB Method is not needed and should not be applied. If the EB Method is applied to individual roadway segments and intersections, and some roadway segments and intersections within the project limits will not be affected by the major geometric improvement, it is acceptable to apply the EB Method to those unaffected segments and intersections.
If the EB Method is not applicable, do not proceed to the remaining steps. Instead, follow the procedure described in
the Applications section of the applicable Part C chapter.
12/16/2009
Presentation Notes
HSM Training Module 11: Predictive Method Specialized Procedures
Module 11 - 17

## Slide 18: CRF Limitations
Sites with low AADTs tend to move to the top
No accounting for sites with zero crashes
Crash rates may be misleading
Doesn’t address regression-to-the-mean bias
Doesn’t account for all roadway elements (lane width, shoulder width, etc.)
Is there a better way?

## Slide 19: Can we use the HSM in place of CRF?

## Slide 20: Regression Model – Safety Performance Function
  where: SPF = predicted number of crashes
  L = section length
  a and b are coefficients that describe the behavior between length, AADT and the estimated number of crashes
(Consider this the average crash rate for a specific road type)

## Slide 21
Chart: SPF Comparison
(Consider this Table 5)
Notes: Kentucky

## Slide 22: SPF Model Parameters
Input:
  section length
  AADT
  Number of crashes
    Severity, Crash Type
Output
  a, b, overdispersion parameter
Notes:   Negative binomial, R uses theta (phi) and SAS uses K (1/phi)

## Slide 23: Empirical Bayes Estimate
Crashes (corrected for regression to the mean)
EB = (Weight)×SPF+(1-Weight)×Observed Crashes
(Consider this the critical crash rate for a specific site)
Notes: Avoid RTM

## Slide 24: Potential for Crash Reduction
Observed Crashes
EB Crashes (Corrected)
Predicted Crashes from SPF
PCR
Crashes per year
AADT
(Consider this the Critical Rate Factor – CRF - for a specific site)
Notes: Note that all of for specific site

## Slide 25: Potential for Crash Reduction
More reliable, science-based approach to highway safety
Addresses regression-to-the-mean bias
Accounts for roadway geometry
Value of PCR can be related to crash costs

## Slide 26: Crash Data Access Tool Demo
(end with crash accuracy demo)

## Slide 27: Location Errors
A need for quality control on lat/long and milepoint

## Slide 30: MFN: 71578305
March of 2016
092-WN-9007 -000 @ 46.28
37.44328, -86.86231
Actual location of 46.28 is:
  37.42090172, -86.83671179
11036.1 feet or 2.09 miles away!!

## Slide 31
MM 48.4
MM 46.28

## Slide 36: Quality Control Study Proposed
Evaluate locations of crashes and update lat/long and/or milepoint
Check for other common errors as well
Data will be stored in BILL but Submitted to TED

## Slide 37: Next Steps for CDAT
Continue to add functionality
Eventually display SPF and calculate PCR
Currently SPF data provided case by case using Kentucky’s Traffic and Safety Data Service:
  http://ktsds.ktc.uky.edu
  Greenup County

## Slide 38: Feedback

## Slide 39: Questions?
Tracy Lovell, KYTC-D07
Tracy.Lovell@ky.gov
Eileen Vaughan, KYTC
Eileen.Vaughan@ky.gov
Eric Green, UK
Eric.green@uky.edu