## Slide 1
Presented at the 2015 ACEC-KY/FHWA/KYTC Partnering Conference
Tom Creasey, PE, PhD
September 9, 2015
Models: Keeping the Horse before the Cart

## Slide 2
“If all you have is a hammer, everything looks like a nail.”
Paraphrased from
The Psychology of Science
Abraham Maslow, 1966

## Slide 3
We make multi-million-dollar investment decisions based on the answers we get from models, but how do we know if the answers are right? And are we answering the right questions?

## Slide 4: Levels of Analysis
High Level
Medium Level
Low Level
Resources
Required
Precision
of Estimate
Direct Field Measurement
Microscopic Simulation
Deterministic Analysis
Sketch Planning
Source: NCHRP 7-22, Planning and Preliminary Engineering Applications Guide to the HCM
Areawide
Multi-Facility
Single Facilities
Corridors
Segments
Points
Accuracy

## Slide 5: Model Categories
Sketch Planning Tools
Travel Demand Models
Analytical/Deterministic Models
Traffic Signal Timing/Optimization Models
Traffic Simulation Models
Integrated Traffic Analysis Tools

## Slide 6: Model Categories and the Project Development Spectrum
Planning
Preliminary
Engineering
Design
Construction
(Traffic Control)
Operations
Preservation
Maintenance
Reliability
Performance Monitoring
Where do you fit in?
How good is your understanding of the tools
available in your area?
Travel
Demand
Models
Sketch
Planning
Tools
Traffic
Signal
Timing
Analytical/Deterministic Tools
Traffic Simulation Models
Performance Monitoring
Reliability

## Slide 7: Model Definition
A system of postulates, data, and inferences presented as a mathematical description of an entity or state of affairs; also: a computer simulation based on such a system (Merriam-Webster Dictionary)
Software
Automation of the model for the sake of efficiency, accuracy and productivity

## Slide 8: Basic Model Types
Deterministic
Stochastic

## Slide 9: Deterministic (i.e. Analytical) Models
No randomness
Always produces same output from given starting condition or initial state (inputs)
Examples
  HCM
  aaSIDRA
  Synchro ICU

## Slide 10: Stochastic Models
Having random probability distribution that may be analyzed statistically but not predicted precisely
Statistically – mean, standard deviation, confidence intervals, etc.
Typically implemented through simulation

## Slide 11: Simulation Models
Macroscopic – based on speed/flow/density deterministic relationships
Mesoscopic
Microscopic
  Incorporates randomness
  “Particle”-based
  Behavioral “rules” (i.e. models) for car following, lane changing, gap acceptance, etc.

## Slide 12: We’re not confined to simulation anymore for:
Arterials/Urban Streets
Interchange Ramp Terminals/Alternative Intersections
Freeway Facilities

## Slide 13: FHWA Traffic Analysis Tools
http://www.ops.fhwa.dot.gov/trafficanalysistools

## Slide 15: Two Areas Where the Industry is Headed
Simplification – HCM Planning & Preliminary Engineering Applications Guide
MAP-21 Performance Measures – especially reliability (SHRP 2 research)

## Slide 16: The Bottom Line
Know your project needs
Know your tools (models)
    What they can do
    What they can’t do
    What it will take (time, effort) to use them
    What you expect to get from them
Select the most appropriate tool for the job

## Slide 17
You wouldn’t buy a car based only on the color. Why would you make a much more costly infrastructure decision based simply on how software looks?

## Slide 18: Questions?