## Slide 1
Not Your Typical Construction Site Storm Water Management
Marilyn Coffey, P.E., CPESC, CFM

## Slide 2
Many SE states (including KY)
  General permits - most sites
  Individual permits – as determined by KDOW, discharge to waters impaired for sediment + approved TMDL
Transportation sites (linear) differ from lots sites (non-linear)
  Differences
  Challenges
Construction site storm water management permits and practices

## Slide 3
Features – Construction Site Lot
c
Notes: Lot-style construction site
Larger construction site open for mass grading, street and utility installation
Later, individual home lot construction would follow.
Pre-construction site generally drains toward the southwest
After construction, site’s drainage may be divided depending on final grading – some may go to curb and gutter drainage along new street, some may still go toward the southwestern corner

## Slide 4: Features – Linear Construction Site
Notes: Linear bridge construction site
Drainage generally flows toward the river
Multiple discharge points for construction storm water to the river – more locations to inspect, more potential “weak points” in erosion prevention and sediment control measures

## Slide 5: Features – Linear Construction Site
Notes: Linear interchange construction site
The interchange is near a drainage divide between the stream to the left and another stream to the right outside the photograph
Multiple discharge points for construction stormwater – toward the stream to the left of the photograph as well as to highway drainage that discharges to the stream just outside the photograph to the right.
This site also is another example of having to inspect more discharge points, more potential “weak points” in erosion prevention and sediment control measures

## Slide 6
Topography
  Steep slopes
  Watershed divides
Sensitive features
  Streams/rivers
  Wetlands
  Sinkholes
  Storm sewer systems
Rainfall differences
  Summer “pop up” thunderstorms
  Amount
  Intensity
Challenge: Spatial Variations

## Slide 7
Topography
  Finish and stabilize steep slopes early
  Monitor for vegetation establishment
Challenge Addressed...

## Slide 8
Sensitive features
  ID key areas early in construction process (and throughout)
  Plan BMPs to protect key areas
    Silt fence with wire backing
    Silt Trap Type C
Challenge Addressed...

## Slide 9
Consider effects of rainfall differences
  Rain gage locations along alignment
  Watch for variable effects along project – consider if BMP adjustments are needed
Challenge Addressed...

## Slide 10
Corridor can cross drainage divides
  Multiple streams
More potential failure points
More discharge points to ID in field
Challenge: Many Discharge Points

## Slide 11
Multiple Discharge Points (Outfalls)
  Improved BMP selection and system function – multiple lines of defense
  Drainage map use and pre-disturbance inspections to ID discharge points
  Targeted training for inspectors and contractors (KEPSC-RI class)
Challenge Addressed..

## Slide 12
Project receives incoming runoff from upslope property
  Overland flow
  Incoming drainage channel (ditch, stream, etc.)
Preferred approach is to divert off-site runoff so it does not go through construction site
  Protect drainage channels
  Less storm water through sediment controls
  Less potential erosion with less runoff over exposed soil
Limited opportunities to divert off-site water for linear sites
  Corridor can hinder use of diversions such as ditches to collect and carry off-site runoff around site
Challenge: Limited off-site runoff diversion

## Slide 13
Look for small-scale opportunities to divert off-site runoff on corridor sites
Plan for BMP system to handle both off-site and construction site runoff where off-site water cannot be diverted
  Multiple lines of defense
  Larger sediment controls to accommodate more runoff
  Extra attention to moving off-site runoff through construction site
Challenge Addressed..

## Slide 14
Corridor site creates challenges for BMP selection
  Expensive to acquire property
  Limited room for larger BMPs such as sediment basins
  Space limitations affect BMP selection, location for dewatering operations
Challenge: Right-of-Way Limitations

## Slide 15
ROW Limitations
  Divert water where feasible (reduce storm water amount to BMPs)
  Install appropriate BMPs to separate construction site drainage from off-site “pass through” drainage (ditches)
  Use BMP selection and system approach
    Pair effective erosion controls and sediment controls
    Multiple BMPs in combination instead of relying only on sediment controls at discharge points
Challenge Addressed..

## Slide 16
Often have traffic moving through construction site
“Windshield inspectors”
  Regulators
  Laymen – public better educated about storm water impacts
Limited public understanding of roadway construction
Challenge: High Visibility Project Sites

## Slide 17
High Visibility Project Sites
  Install and maintain construction exits – avoid drawing unwanted attention to the site due to mud track-out onto travel lanes
  Extra BMP maintenance care/attention, especially adjacent to traveled areas
  BMP selection to avoid BMPs that don’t work well with traffic through a construction site
    KYTC Silt trap Type C - ponded water
    Overflow for higher flows
    May not be compatible with traffic areas
Challenge Addressed..

## Slide 18
Maintaining appropriate site records
Keeping records current
Recognize and address communication problems/issues that affect storm water discharges from site
  BMP type, sizing (such as Silt Trap Type A)
  Location – station, offset
  Right type of BMP for location
  What caused failures, and whether BMP changes are needed as a result
Challenge: Records/Communication

## Slide 19
Good written communication
  KYTC Inspection form
    KEPSC-RI training
    Clear locations
  Consistent with other project records (KYTC – daily work report)
Good verbal communication
  Joint inspection with contractor
  Inspector, contractor, subcontractor personnel
Be prepared for a regulator visit or site audit
  Complete inspection form as soon as possible after inspection
Challenge Addressed..

## Slide 20
Recap..
Linear Site Challenges
Spatial variations
Many discharge points
Limited off-site runoff diversion
Right-of-way limitations
High visibility project sites
Records/communication
Ways to Address
Finish/stabilize steep slopes
Vegetation establishment
ID key areas early and protect
Consider rain gage locations
Better BMP selection/systems
Targeted training (KEPSC-RI)
Handle off-site & on-site runoff
Install/maintain exits
BMP maintenance attention
Good written & verbal communication

## Slide 21
Company Overview
Founded March 1997
  Woman Owned Small Business/Disadvantaged Business Enterprise
KYTC Prequalifications
  Environmental and UST Services
  Construction Engineering Services
Major Service Lines
  Environmental Consulting
  Water & Natural Resources Consulting
  Construction Materials Testing
  Construction Engineering/Inspection & Special Inspections
  Geotechnical Engineering
Office Locations
  Bowling Green, KY
  Nashville & Knoxville, TN
  Pensacola, FL

## Slide 22
Thank You!