## Slide 1: Road Safety Assessments
Wednesday, September 6, 2023
by: Mike Vaughn, PE
in project
development

## Slide 2: Road Safety Assessment Definition:
A formal safety performance examination of an existing or future road or intersection by an independent, multi-disciplinary team.
From FHWA’s RSA webpage:

## Slide 3: Road Safety Assessment Definition:
A formal safety performance examination of an existing or future road or intersection by an independent, multi-disciplinary team.
From FHWA’s RSA webpage:

## Slide 4: Road Safety Assessment Definition:
A formal safety performance examination of an existing or future road or intersection by an independent, multi-disciplinary team.
From FHWA’s RSA webpage:

## Slide 5: Road Safety Assessment Definition:
A formal safety performance examination of an existing or future road or intersection by an independent, multi-disciplinary team.
From FHWA’s RSA webpage:

## Slide 6
Source: FHWA

## Slide 8: RSAs are a great way to implement the Safe System Approach
Safe System Principles
Humans make mistakes
Humans are vulnerable
Death & Serious Injuries are unacceptable
Safety is proactive
Redundancy is crucial
Responsibility is shared
Safe System Elements
Safe road users
Safe vehicles
Safe speeds
Safe roads
Post-crash care

## Slide 9: RSAs are a great way to implement the Safe System Approach
Safe System Principles
Humans make mistakes
Humans are vulnerable
Death & Serious Injuries are unacceptable
Safety is proactive
Redundancy is crucial
Responsibility is shared
Safe System Elements
Safe road users
Safe vehicles
Safe speeds
Safe roads
Post-crash care

## Slide 10: What causes Fatal & Serious Injury Crashes?

## Slide 11: What causes Fatal & Serious Injury Crashes?
The transfer of too much kinetic energy to the human body.
Kinetic Energy = ½ mass x velocity2

## Slide 12: What causes Fatal & Serious Injury Crashes?
The transfer of too much kinetic energy to the human body.
Kinetic Energy = ½ mass x velocity2
As transportation system managers, our number focus need to be:
managing kinetic energy!

## Slide 13: Managing kinetic energy involves:
Managing
speed
Source: Fehr & Peers
Managing
crash angles
Source: City of Carmel, IN
Managing
crash energy distribution
Source: FHWA

## Slide 14: Managing kinetic energy involves:
Separating road users
in space
Source: Fehr & Peers
Separating road users
in time
Source: Fehr & Peers
Increasing road user
awareness
Source: Fehr & Peers

## Slide 15: Managing kinetic energy involves:
Analyzing and decreasing conflict points
Preventing high kinetic energy crash types
Source: KYTC
Source: KYTC

## Slide 16: Are RSAs in Project Development Really New?
Traditional Safety Review
Road Safety Assessment
The safety review team is not usually independent of the project team. | Performed by a team independent of the project.
Typically performed by a team with only design and/or safety expertise. | Performed by a multi-disciplinary team.
Typically focuses on motor vehicle traffic. | Focuses on ALL road users.
Typically does not consider human factors. | Considers human factors and the capabilities and limitations of the various types of road users.
May not generate a formal report. | Always generates a formal report.
Often does not generate a formal response report. | A formal response report is an essential element.

## Slide 17
Promotes awareness of safe design practices across KYTC and our partners
Helps produce designs that lower the frequency and risk of severe crashes
Gives project teams another opportunity to consider multimodal safety concerns and integrate multimodal best practices
Benefits of RSAs in
Project Development

## Slide 18
An excellent opportunity to consider both human factors and human behaviors for all road users in all facets of a project’s design
  Human factors are the capabilities and limitations because we are human
    I can’t see through a tree (I’m not superman)
    We absolutely must design for human factors
  Human behaviors are things in which we choose to do
    The speed I drive my vehicle is a choice
    Our designs may not perfectly control human behaviors, but our designs can have an influence
Benefits of RSAs in
Project Development

## Slide 19
Can lower overall project lifecycle costs
  Less maintenance costs (e.g. flattened roadside slope vs. guardrail)
  Less future reconstruction costs
    It’s much more expensive to tweak the design after a project is constructed and in-service vs. adjusting during the D phase
  Less societal costs
    Fewer severe crashes
    Less severe crashes = fewer liability claims for KYTC and our partners, insurance companies, and ultimately the public
Benefits of RSAs in
Project Development

## Slide 20
FHWA’s RSA Resource webpage:
https://highways.dot.gov/safety/data-analysis-tools/rsa/rsa-resources
RSA Resources

## Slide 21
FHWA’s RSA Resource webpage:
https://highways.dot.gov/safety/data-analysis-tools/rsa/rsa-resources
RSA guidelines
Ped & bike RSA guidance and prompt list
Using IHSDM in the RSA process
Using 3-D visualization in the RSA process
  As we get better using ORD, I suspect 3-D visualization will become easier and extremely useful for RSAs in project development
RSA Resources

## Slide 22
Identification of roadway elements (or lack of elements) that may present a safety concern
  To what extent
  To which road users
  Under what circumstances
Identification of potential safety improvement opportunities (no matter how small or large) to mitigate identified safety concerns
Why RSAs in Project Development

## Slide 23: Questions?
Contact info:
  Michael Vaughn, PE
  Traffic Safety Branch
  Division of Traffic Operations
  Kentucky Transportation Cabinet
  Mike.Vaughn@ky.gov