## Slide 1: ddSAFCAT: Quantifying Safety of Automated Vehicles Reg Souleyrette, Austin Obenauf, Freddy Lause KTC/Civil Engineering, Univ. of Kentucky

## Slide 2: Automated Vehicles Will Save Lives, but …
How many?
When?
Knowing these things could …
  Spur investment (private) – a bit of a chicken and egg
  Inform policy and regulation (public) – more chicken and egg
  Change safety “planning” and investment (public)
    Engineering
    Enforcement
    Education
    Emergency Response
How to know?

## Slide 3
https://en.wikipedia.org/wiki/Motor_vehicle_fatality_rate_in_U.S._by_year#/media/File:US_traffic_deaths_per_VMT,_VMT,_per_capita,_and_total_annual_deaths.png
How many lives could be saved?

## Slide 4: Safety the problem, CAVs the solution?
They say 94% of crashes are due to human error…
Can CAVs address all human factors?
In the long run even, some things might be “worse” …
“The human error components of walking, biking, motorcycle use will not be completely mitigated even with perfect automated vehicles. Also there is a residual category of tree falls on car, sinkhole, washed away in flood, suicide by auto, that won't be mitigated by smart cars” – S. Polzin, personal correspondence
Notes:   Money spent on AVs could be spent on less-expensive “safer” cars
  Money spent on making the infrastructure work with AVs and CAV-tech enabled cars could be spent making roads safer for non-CAVs*
  Interactions between AVs and non-CAVs may be more dangerous than a driver-operated system
  Effectiveness requires proper use, can be a distraction, users compensate for risk
* some improvements may help both types of cars

## Slide 5: But … Automated Vehicles Will Save Lives
How many?
When?
Knowing these things could …
  Spur investment (private) – a bit of a chicken and egg
  Inform policy and regulation (public) – more chicken and egg
  Change safety “planning” and investment (public)
    Engineering
    Enforcement
    Education
    Emergency Response
How to know?

## Slide 6
https://www.rand.org/pubs/tools/TL279/tool.html
Autonomous Vehicle Safety Scenario Explorer
Really?*
*even with no full AV, the safety curve would probably bend down (blind spot warnings, stability control, automatic braking, etc. )
link

## Slide 7: AV component technologies

## Slide 8: How exactly do CAVs affect Safety?

## Slide 9: Time-Variant CAV Safety Performance
Initially, mixing in AVs may make things worse (for some crash types)
22 of 26 reported AV accidents, AV not at fault (CA crash study)
video
  Interactions with non-CAVs

## Slide 10
video
Risk compensation
Distractions
Proper
Utilization

## Slide 11: Automated Vehicles Will Save Lives
How many?
When?
Knowing these things could …
  Spur investment (private) – a bit of a chicken and egg
  Inform policy and regulation (public) – more chicken and egg
  Change safety “planning” and investment (public)
    Engineering
    Enforcement
    Education
    Emergency Response
How to know?

## Slide 12: State of the Art Safety Data Analytics
Highway Safety Manual
Finally getting folks to accept Empirical Bayes (not everyone)
Some researchers pointing out limitations (exposure, temporal effects)
All assume static technology* – not even time series…
  Sort of like estimating auto safety
  using past performance of the horse!
* Also a problem for design standards, e.g., Green Book

## Slide 13: Let’s look back … Issues in 1900:
Notes: Cars provided mobility, space and status
They were viewed as being safer than horses
Scientific American, 1900 “If there are faults with cars, only time is wanted to make them disappear … there is no mechanism more inoffensive, no means of transportation more sure and safe
Unlike horses, cars wouldn’t run away, bite or kick their owner, plus they were less costly to maintain
Less manure and airborne bacteria - By the1920’s, when cars had replaced horses, tuberculosis rates dropped
Horses stabled away from carriages, prediction of NYC 10’ deep in horse manure,
land for oats …

## Slide 14: Horses were a real problem
I don’t think that was justified

## Slide 15: They bit, kicked and ran over people…
Notes: Cars provided mobility, space and status
They were viewed as being safer than horses
Scientific American, 1900 “If there are faults with cars, only time is wanted to make them disappear … there is no mechanism more inoffensive, no means of transportation more sure and safe
Unlike horses, cars wouldn’t run away, bite or kick their owner, plus they were less costly to maintain
Less manure and airborne bacteria - By the1920’s, when cars had replaced horses, tuberculosis rates dropped
Horses stabled away from carriages, prediction of NYC 10’ deep in horse manure,
land for oats …

## Slide 16: They transmitted tuberculosis…

## Slide 17
Human food cost increase due to competition from feed production

## Slide 18: And, it’s real hard to think beyond something like this …
http://www.hhhistory.com/2017/08/the-great-manure-crisis-of-1894.html

## Slide 19: The vision for cars …
“If there are faults with cars, only time is wanted to make them disappear … there is no mechanism more inoffensive, no means of transportation more sure and safe”
Notes: Cars provided mobility, space and status
They were viewed as being safer than horses
Scientific American, 1900 “If there are faults with cars, only time is wanted to make them disappear … there is no mechanism more inoffensive, no means of transportation more sure and safe
Unlike horses, cars wouldn’t run away, bite or kick their owner, plus they were less costly to maintain
Less manure and airborne bacteria - By the1920’s, when cars had replaced horses, tuberculosis rates dropped
Horses stabled away from carriages, prediction of NYC 10’ deep in horse manure,
land for oats …

## Slide 20
But, what really happened?

## Slide 23: But … Automated Vehicles Will Save Lives
How many?
When?
Knowing these things could …
  Spur investment (private) – a bit of a chicken and egg
  Inform policy and regulation (public) – more chicken and egg
  Change safety “planning” and investment (public)
    Engineering
    Enforcement
    Education
    Emergency Response
How to know?

## Slide 24
https://www.rand.org/pubs/tools/TL279/tool.html
Autonomous Vehicle Safety Scenario Explorer
Really?*
*even with no full AV, the safety curve would probably bend down (blind spot warnings, stability control, automatic braking, etc. )
link

## Slide 25: How ’bout some more dials?
Don’t we already have enough?

## Slide 26: What will cause crash reduction/increase, how, when and how much?
Distractions
Proper
Utilization
  Interactions with non-CAVs
Notes: Update this slide

## Slide 27: F=F0 x GVMT x (1-MPAV) x (1-CRFAV) x MPCAV tech x (1-CRFCAV1) x (1-CRFCAV2) x …
Logistic Function
A is the lower limit, K is the upper limit
B is the growth rate
t represents the current year
M represents the year of 50% “penetration”
SATURATION?
WHEN?
WHEN?
Reduction in Fatalities = f(market penetration, effectiveness)
Notes: Gathering formulas now

## Slide 28
Market Penetration = f (cost, regulation, acceptance…)
Effectiveness = f(technology, other factors)
  Road system
  Crash type
  Crash conditions (e.g., environmental)
  Causal factors
    Proper Use = f(behavioral, quality, effectiveness, ease…)
    Risk Compensation = f(behavioral, other)
    Distraction = f(behavioral, familiarity, user interface quality/maturity, …)
Subject to … limits, interactions, etc.
Notes: Gathering formulas now

## Slide 29
Notes: update

## Slide 30
Assumes …
AVs all the same All roads the same All crashes the same
Notes: Associate with %s of drowsy/distracted driving, rear ends, side swipes, and lane/road departure

## Slide 31
Notes: Associate with %s of drowsy/distracted driving, rear ends, side swipes, and lane/road departure

## Slide 32
Inform with data!
Notes: Associate with %s of drowsy/distracted driving, rear ends, side swipes, and lane/road departure

## Slide 33
Interstates
Arterials
Local
Collectors
Inform with data!
Notes: Associate with %s of drowsy/distracted driving, rear ends, side swipes, and lane/road departure

## Slide 34
Interstates
Arterials
Local
Collectors
Inform with data!
Notes: Associate with %s of drowsy/distracted driving, rear ends, side swipes, and lane/road departure

## Slide 35: Automated Vehicles Will Save Lives
How many?
When?
Knowing these things could …
  Spur investment (private) – a bit of a chicken and egg
  Inform policy and regulation (public) – more chicken and egg
  Change safety “planning” and investment (public)
    Engineering
    Enforcement
    Education
    Emergency Response
How to know?

## Slide 36
State of the Art Safety Data Analytics
Highway Safety Manual
CMFs
CMFs with CAV penetration > CMFs now (likely)
Some CMFs with CAV penetration < CMFs now (in a few cases)

## Slide 37: Questions/suggestions?
Thank you
Music city bowl pic
https://xkcd.com/1958/