ESheet Macro Tips

As the time approaches to submit right of way or final plans, you may need to cut eSheets for plotting.  An eSheet macro has been created that will make this process a lot easier than manually clipping, exporting to 2-D, rotating, etc.  The newest version of the macro was created to work with the new (2005) CADD standards.

Before you get started…

- Software Requirements include the latest version of CADD Standards which you can download from the following website:

http://www.kytc.state.ky.us/CADDstandards/

- You will need to make sure that all sheet borders are cells from the new sheet cell library that was downloaded with the new CADD standards.  If you need to attach the new cell library, it can be found in the following directory:

C:\Program Files\Bentley\Workspace\Projects\KYTC Resource\cell

- For the eSheet macro to work, the sheet cell must remain intact.  Do not drop the sheet cell.

- All files must have the correct document name in the datafield located in the left hand corner of the sheet cell.  This will be the name of the file you create.

- All the files you are going to cut as eSheets must be exported out of Projectwise onto your hard drive.  The current eSheet macro does not work with Projectwise.

- There can be only one view open in your .dgn file.

- Make sure the fence mode is set to inside.

- There should be no extra sheet cells in your file.  The macro will plot anything in the correct sheet cell.

Now, you should be ready to get started.  Open up the drawing you wish to make into an eSheet.  If you do not already have this toolbar displayed,

you will need to go to Tools>Customize and then click on the Toolbars tab.  Check on the KYTC Software toolbar.

Click on the symbol with the e.  You should see the following dialogue box:

In most cases you will want to toggle on Automatic.  Click Create eSheets.

If you have raster images attached, you may get a raster message.  If this is the case, click ok.  The macro should process the eSheet and a message will pop up giving you the process time.

Click OK.  You should still be in your original file.  The eSheets macro has placed the newly created eSheet in a subfolder to the folder your original file is in.  The subfolder will be name eSheets.

The esheets macro also works when there are multiple sheets in a file, such as a set of cross sections.  The first time you cut eSheets in this situation, use the Automatic option.  It will create a sheet for every sheet cell.  If one of the sheets in the set needs to be recut, use the Single eSheet option.  You will be prompted to click on the border of the sheet you want to recut.

You will be warned that the file already exists and will be overwritten.  Click OK.  Your new eSheet will be created.  The Multiple eSheet option works very similar to the Single eSheet option.  However, it allows you to choose more than one sheet to recut.

Once your eSheets are cut, you can move them to Projectwise.

If you have any questions on how to use the macro, please contact Jill Asher.  If the macro does not seem to work properly, i.e. technical difficulties, please contact Henry Wells, the creator of the macro.  Both can be reached at (502) 564-3280.